## Slide 1: Intra-Day Trading Working Group 3
<number>
Notes: *
*
<number>##

## Slide 2: Additional Option
<number>
Two Additional Ex Ante Runs EA2 (15:00) and EA3 (18:00)
One within Trading Day run WD1 (12:00)
EA3 schedule fixes MIUNs for first 12 hours of Trading Day D (06:00 to 18:00 of D)
WD1 will have a 30 hour Optimisation Time Horizon (running from 18:00 of D to 00:00 of D+1)
Notes: Timings of EA2 and EA3 are suggested but could be modified.
*
*
<number>##

## Slide 3: Timeline
EA1
GC
10:00
EA1
pub
06:00
17:00
06:00
EA2
GC
WD1
pub
18:00
D-1
D
11:00
14:00
15:00
18:00
WD1
GC
MIUNs for this period set by EA3
EA2
pub
EA3
GC
EA3
pub
06:00
11:00
12:00
OTH for WD1
D+1
06:00
00:00
Notes: *
*
<number>##

## Slide 4: Timeline (cont’d)
<number>
GC = Gate Closure
GO = Gate Opening
EAn = Ex-Ante Market Schedule
WDn = Within Day Market Schedule
Notes: SEMO proposal on Intra-Day Trading
This proposal builds on modification Mod_18_10. It includes two extra Ex-Ante runs as did the modification, listed in the diagram above as EA2 and EA3. The proposal also introduces a within day run of the UUC, designated WD1.In the diagram above, the respective Gate Openings, while listed at the same time as the publication of the previous schedules, are assumed to be as early as possible after the publication and may actually be later to account for modification of Interconnector User Nominations into MIUN.
As per the proposed modification, the EA1 schedule will set IUN/MIUN for Interconnector Users with firm capacity holdings secured in the separate auction. These allocations can be protected in later runs by Participant bidding. Should Participants wish to unwind this position, they can do this by bidding themselves back out of merit in later auctions.
The suggestion is for the timing of EA3 to be at 18:00, to ensure that schedules for the Interconnector can be closed out 12 hours before the start of the Trading Day at 6AM. This will ensure that the interconnector schedule can be accommodated with respect to generators with a start-up notification time of 12 hours, in cold state. The results of this schedule, in terms of interconnector MIUNs, will then be fixed for the first 12 hours of the Trading Day.
*
*
<number>##

## Slide 5: Questions
<number>
I/C Users only re-bidding?
Additional Ex Ante runs on D-1?
Changing Optimisation Time Horizon
SO Constraints
Complexity
Notes: Following this, after the start of the Trading Day, a Within Day run of the MSP software (WD1) will be completed. This run will have a thirty hour optimisation horizon, starting from 18:00 running to midnight the following day (D+1). This run follows on from the previous runs, with MIUN allocations from the EA2 and EA3 runs held protected unless the Participant elects to bid out of their position.
While introducing some limitations around the Within Day schedule, this still adheres to the basic principal of the SEM being an unconstrained pool market. The commitment decisions held as firm in the Within Day schedule are based on Ex-Ante runs which are totally unconstrained. This version does not attempt to address constraint issues or security of supply issues around the firm allocation of energy on the interconnector. It is expected that if it is required to alter the flow of an interconnector for security of supply issues, this should be managed through some form outside of market arrangements to be developed in separate workstreams.
.
*
*
<number>##