## Slide 1: Scheduling & Dispatch
Stakeholder Engagement
Industry Workshop
06 September 2023
This presentation provides an update on the Scheduling & Dispatch Programme.
  Achievable – Valuable – “Simple”

## Slide 2: Scheduling & Dispatch: Industry Workshop (September 2023) Agenda for today’s workshop
Time | Topic
13:00 | Introduction
13:15 | Programme Overview
13:45 | Functional Changes Explained
14:45 | Market Arrangements Changes
15:00 | Stakeholder Engagement
15:15 | Systems Delivery Update
15:30 | Additional Q&A AOB
Additional detail on functional changes
On schedule for MODS changes (ESPS)
Preparing MODS changes (NPDR, WDT)
Progressing integrated delivery plan (with key milestones)
Engaged with technology vendors on detailed design for system changes
Programme staffing and support
Since We Last Met

## Slide 3: Scheduling & Dispatch Programme– Industry Outreach
Why Are We Here?
Discuss
We will discuss the functional changes and how this impacts you and your portfolio. We will discuss the formal arrangement changes, stakeholder management, and the delivery schedule. We are happy to field all questions – and we may not be able to answer all of them today.
Inform
We are here is to provide information about the ongoing work with the SDP initiatives and the impact on the market participant community. We will provide a view of the programme’s drivers, functional details, structure, timelines, and stakeholder engagement.
Ask
We will ask for your participation throughout – we are better together.
Listen
We are here to listen. What are you thoughts on the SDP, the functional details and the impacts to your business? What questions do you need answers to? What clarity do you need?

## Slide 4: Scheduling & Dispatch Programme – Industry Workshop
Setting Expectations
Meeting Rules
Engage: actively listen and ask questions. This session is for you.
Show Courtesy: allow everyone the time and space to participate in the discussion. Don’t talk over another speaker.
Scope Discipline: maintain focus on SDP. No specific technology discussion today.

## Slide 5: Scheduling & Dispatch Programme Overview
SDP Objective & Drivers
To enhance and improve the technology and capability of scheduling and dispatch in Ireland and Northern Ireland. This is driven by market participant needs, the EU Clean Energy Package mandates, and in support of the broader goals of renewables and System Non Synchronous Penetration (SNSP) penetration targets.
Clean Energy Package requirements – NPDR treatment
Ireland and Northern Ireland Government renewables targets for the 80%/70% total renewable energy and 95+% system non-synchronous penetration (SNSP) on an instantaneous basis.
Market Participant requests for certainty on treatment of renewable assets, batteries – revenue certainty.
Market Participant requests for improvement in re-balancing and re-dispatching (prevailing weather).
  One component of the broader SOEF programme.
  SDP_001: Operation of non-priority dispatch of renewables (NPDR)
  SDP_002: Energy Storage Power Station (ESPS) integration
  SDP_003: Fast Frequency Response (FFR)
  SDP_004: Wind/solar dispatchability improvements
  SDP_005: Reserve services scheduling and dispatch
  SDP_006: Synchronous condenser scheduling and dispatch
Scope of SDP
For this complex programme…
  Be pragmatic about solution pathways.
  Solve the immediate and urgent problems at hand.
  Don’t allow perfect to be the enemy of good.
  Communicate early and often – to all stakeholders.
  Maintain support of industry.
  Actively manage multidisciplinary delivery team.
  Achievable – Valuable – “Simple”
Key Principles
Delivery Groupings
  Group 1
  SDP_001
  SDP_002
  SDP_004
  Group 2
  SDP_003
  SDP_005
  SDP_006
SDP Timeline
TBC
Today
Detailed Design
Analysis
Readiness and Rollout
Implementation
SDP Group 1 Go-Live

## Slide 6: Stakeholder Engagement: Industry Workshop
A programme structure consisting of 5 workstreams has been put in place for Phases 2-5
Dedicated S&D manager and team in place
Resources deployed across 5 workstreams:
External support provided by Accenture (programme management) and Market Reform (markets expertise)
Support to the Programme is being provided from across EirGrid & SONI e.g. TSO and MO Operations, IT
Central & Market Arrangements
Focus on changes to Grid Code, TSC, CMC as a result of SDP changes. EirGrid led, leveraging existing MOD processes
Systems Delivery
All aspects of systems design, development and rollout. Participant connectivity, data readiness, and go-live.
External Stakeholder Engagement & Readiness
Engaging, supporting, and measuring external readiness. Continuous engagement via bilateral and group meetings. Key principle: stay engaged!
Operational Capability
Internal business preparation for enabling the SDP changes.
Programme Management
Dedicated PM lead for SDP, coord. w/ Head of Future Markets
Programme Structure

## Slide 7: SDP_001: NPDR Units
Functional Component | What’s New or Changed
Registration and Input Data | Generator ramp rates are considered to be infinitely high NPDRs will submit TOD, COD, PNs and forecasts (which can then be used in the TSO forecasting process and in scheduling) Mandated zero price for Startup and No-Load
Scheduling and Dispatch | NPDRs will be scheduled economically based on TOD/COD/PNs (in conjunction with all other units) NPDR dispatch by the Control Rooms will be based on Merit Orders derived from scheduling consistent with thermal units NPDRs will always have a control setpoint in place and be subject to active power control
Pricing | Instruction profiling will take into account Constraint, Curtailment and Merit Order (MWOF) instructions for NPDRs MWOF instructions and subject to continuous open acceptance until the next adjacent MWOF instructions Prices for MWOF actions will be based on submitted COD
Settlement | Settlement will be as for conventional units. One special note is the Fixed Cost Payment or Charge will always be zero, due to the mandated zero value for start-up and no-load costs.
Reporting | Data for NPDR Units will be integrated into existing reports. No material changes to any existing report.
Summary | NPDRs will, insofar as possible, be treated like thermal generator units for energy balancing. NPDRs will be subject to constraint and curtailment with priority dispatch units. Priority Dispatch renewable generators continue under existing arrangements and may choose to re-register as NPDR Units.

## Slide 8: SDP_001: Scheduling Approach
Renewable forecasts
  Control centre engineers will be able to better utilise external forecasts from vendor and/or availability submitted by Participants via the MPI
  Additional flexibility for control centre engineers to enable greater control of weighting and blending of forecasts from different forecast vendors / participant-submitted availability
Scheduling
  NPDR units will be scheduled based on submitted COD, TOD, and PN (and will have zero start-up costs and no-load cost)
  NPDR units will be considered ON where their generation forecast is > 0
Dispatch
  Given the volume of NPDR Units, they will be grouped within control room online merit orders, grouped into price bands
  Control centre engineers will be able to select constraint, curtailment or merit order (MWOF) actions

## Slide 9: SDP_001: Implications for Instruction Profiling/QBOA
Profiling of wind/solar units is currently summarised as follows:
  FPN = real-time availability
  Constraints and curtailment are always dec actions and profile to the lower of their MW target and availability
  Profiles for constraints and curtailment (LOCL, CURL) ramp instantaneously
  Constraints and curtailments can be active simultaneously and are profiled in order of issuance
  Closure of constraints and curtailment is achieved via issuance of closing instructions (LCLO, CRLO)
As a result of SDP_001:
  For Priority Dispatch renewables, nothing changes (treatment will continue to be as set out above)
  NPDRs will always have an MWOF instruction in place (and may also have curtailment/constraint)
The introduction of NPDRs means that these units will be able to receive three types of dispatch instruction:
  LOCL, with corresponding LCLO to close
  CURL, with corresponding CRLO to close
  MWOF, issued by control centres to the lower of a merit order set point and availability
For NPDRs, there must be new logic for correct treatment of constraint, curtailment and balancing actions.

## Slide 10: SDP_001: Proposed Instruction Profiling Approach for NPDRs
We will have the ability to create energy balancing, constraint and curtailment profiles simultaneously and identify the reason for each action to apply the correct price.
Continuous open acceptance of MWOFs and pseudo instructions until next adjacent MWOF or pseudo instruction is issued (adjacent meaning not separated by CURL/LOCL).
LOCL/CURL/LCLO/CRLO instructions to be profiled as today.
Instantaneous ramping for all actions.
Energy balancing profiles will be ordered based on effective time of the relevant MWOF

## Slide 11: SDP_001: Example Case for NPDR Instruction Profiling
Time (minute) | Type | MW
5 | MWOF#1 | 80
6 | LOCL | 60
8 | CURL | 50
11 | MWOF#2 | 35
19 | MWOF#3 | 45
120
100
80
60
40
20
FPN
o=1
o=2
o=3
o=6
o=5
5
10
15
20
25
o=7
o=8
o=4

## Slide 12: SDP_001: Day in the life
Submit NPDR Units transaction data
TSO receives/utilises external renewable forecasts
TSO determines indicative generation schedules (LTS, RTC, RTD)
Indicative schedules are used to derive Inc/Dec Merit Orders
Control Room(s) make dispatch decisions (all Units, including NPDRs)
Approved setpoints issued to NPDRs (~DIs), via WDT
COD (PQ pairs [zero fixed costs]) and TOD set selection
Physical Notifications (stepwise)
Forecast Availabilities
Indicative operations schedules are an optimised view at point in time of how demand can be met whilst minimising deviation from PN, and whilst meeting all of the necessary constraints (e.g. reserve, inertia, transmission network capability)
NPDRs always are subject to setpoints from the TSO
Pricing and imbalance settlement (based on DIs, PNs and metering)
New profiling logic, to take account of the fact that NPDR Units can be subject to any/all of (a) curtailment, (b) constraint, (c) merit order setpoints
For NPDR units, Control Room decisions may result in (a) merit order-derived targets, (b) curtailment, or (c) constraint

## Slide 13: SDP_002: ESPS Units
Functional Component | What’s New or Changed
Registration and Input Data | Registration Registration – Register as battery units under trading site Minimum and Maximum Storage Capacity (MWh). Maximum Generation (MW)*, Registered Minimum Output (MW)* (*existing) COD Minimum and Maximum Storage Capacity (MWh) (Validation against Registered Min/Max Op Storage Limits) Prior Day End Storage Level (a day ahead view of the storage level in MWh for ESPS Units, which must be able to change on a daily basis in advance. (VTOD, Agreed Proc., App 4) Physical Notifications can have negative MW QTY values (representing charging state). Incremental and Decremental Price and Quantity Curves for Complex and Simple COD are to cover the full operating range from charging (negative MW QTY) to generating (positive MW QTY). Data Validations of Note: Forecast availability profile (>= 0) Forecast minimum output profile (<=0) Forecast minimum stable generation profile (all zero) Start-up, shut-down and no-load costs submitted but mandated to be zero. PNs of zero MW will be interpreted as “ON at zero” (As opposed to “OFF” like conventional generators.)
Summary | For ESPS units (and we are fundamentally talking about batteries in this SDP), the intention is to provide more control and assurance for market participants in the use of batteries, and great visibility and usefulness of the battery assets to the TSO control Centre engineers, within the Scheduling and Dispatch processes.

## Slide 14: SDP_002: ESPS Units
Functional Component | What’s New or Changed
Scheduling and Dispatch | ESPS scheduled based on the generator PN (“Follow PN” mode) by default. Control Centre Engineers may move them to manual scheduling – only when necessary. Note: If a PN (or culmination of PNs violate transmission security constraints, this is a case where PNs would be moved, to relieve the constraint) If an ESPS Unit is dispatched away from its PN, it remains the responsibility of the Market Participant to update the PN and manage the energy available for the ESPS Unit. Scheduling and Dispatch Operators will dispatch ESPS Units back to their PN before resetting to “Follow PN” mode. A PN feasibility assessment will apply to ESPS PNs. This will occur after submission – and only within the control centre. Pending vendor design, Dispatch Instructions for charging may be negative MW QTY.
Summary | For ESPS units (and we are fundamentally talking about batteries in this SDP), the intention is to provide more control and assurance for market participants in the use of batteries, and great visibility and usefulness of the battery assets to the TSO control Centre engineers, within the Scheduling and Dispatch processes.

## Slide 15: SDP_002: ESPS Units
Functional Component | What’s New or Changed
Pricing (Balancing Market Price Formulation) | ESPS Units can operate below their Minimum Stable Generation (mandated to be zero). They will be Non-Marginal Flagged (as is the case now) if operating at or below their LOL, operating at their HOL, or ramp constrained. Non-energy flagging tests will be modified so that they check whether QRTD is non-zero, rather than greater than zero as for conventional Generator Units.
Settlement | Settlement changes - Decoupling from treatment of pumped storage (affecting various payments/charges), handling negative values (e.g. CTEST), using Min Output as floor for inc QBOA calculations
Reporting | Additional reports will be included for ESPS Units, to show energy and reserve schedules by reserve type, system wide, in aggregate and individually.
Summary | For ESPS units (and we are fundamentally talking about batteries in this SDP), the intention is to provide more control and assurance for market participants in the use of batteries, and great visibility and usefulness of the battery assets to the TSO control Centre engineers, within the Scheduling and Dispatch processes.
Additional note: We are currently investigating how Long Duration Energy Storage can be facilitated by these changes. Much will depend on the commercial and technical discussions on LDES treatment, currently in-flight with the TSOs, RAs, and participants.

## Slide 16: SDP_002: Day in the life
Submit Unit transaction data
PN feasibility is tracked and alerted to Control Centres
ESPS units are included in Control Centres Merit Orders
Control Centre makes dispatch decisions
Approved DIs issued to ESPS units, via EDIL
COD (fixed costs=0, PQ pairs to cover entire range from charging to discharging), TOD set selection
Physical Notifications (piecewise)
Forecast Availabilities (with min stable gen = 0)
Operational storage min/max
Pricing and imbalance settlement (based on DIs, PNs and metering)
Control Centres respond where “follow PN” is not appropriate
Amended flagging rules to allow for ESPS units in negative generation range
Some minor amendments to settlement equations to allow for negative range for ESPS (treatment will not be based on pumped storage)
Dispatch decisions deviating from PNs may cause re-evaluation by the party of its ex-ante position

## Slide 17: SDP_004: Wind/Solar Dispatchability Improvements
Functional Component | What’s New or Changed
Rebalancing / Redispatch | Use weather conditions (in the form of changes in availability) to enable rebalancing of constraint and curtailment to Priority Dispatch and Non-Priority Dispatch Renewable Units Enable Control Centres to utilise existing tools to more effectively apply, relax and remove constraints and curtailments through issuance of control setpoints
Reporting | Calculation of jurisdictional dispatch down ratio based on real-time availability data for Control Centre awareness Reports including enhanced detail into the standardised reasons for constraint/curtailment decisions
Summary | To improve the rebalancing of intermittent renewables based on changing weather conditions

## Slide 18: SDP_004: What is rebalancing? Why is rebalancing important?
CURRENT APPROACH TO APPLICATION/REMOVAL OF CONSTRAINT AND CURTAILMENT:
Application: “Active Power Control setpoints are both calculated on the basis of distributing a reduction in output between price taking generation unit in tie break using the Active Power output of each price taking unit in tie break to be curtailed or constrained”
Removal (part or all): “Active Power Control setpoints are calculated on the basis of distributing an increase in output between price taking unit in tie break on a pro-rata basis whilst ensuring that following the removal of a curtailment the Active Power Control setpoint for no unit exceeds any constraint setpoint that was already in place”
WHAT IS REBALANCING? WHY IS REBALANCING IMPORTANT?
Rebalancing is a process by which redistribution of Curtailment or Constraint is performed
Discussions with various parties with renewable generator units have confirmed that the current approach to application of Constraint and Curtailment does not take appropriate account of prevailing weather conditions
Effective rebalancing should utilise weather conditions (in the form of unit availability, Available Active Power) to regularly redistribute constraint and curtailment to affected renewable units
Extract from SEM-13-011
CURRENT DEFINITIONS OF CONSTRAINT AND CURTAILMENT:
Constraint: “If the Control Centre assumed it had control over every price taking generation unit in tie break on the island of Ireland and the security issue presented could only be resolved by reducing the output of one or a small group of price taking generation units in tie break then that reduction is deemed a constraint and logged as such”
Curtailment: “If the Control Centre assumed it had control over every price taking generation unit in tie break on the island of Ireland and the security issue presented could be resolved by reducing the output of any or all of the price taking generation units in tie break then that reduction is deemed a curtailment and logged as such”
Extract from SEM-13-011

## Slide 19: SDP_004: “Day in the life”
Weather conditions change over time
Renewable unit availabilities change (telemetry)
Control Room notified of scope for rebalancing
Control Room can initiate rebalancing
Control Room reviews and can approve rebalanced setpoints
Approved setpoints issued to affected units
Automated
Control Room(s)
Important:
Rebalancing is initiated and enacted via the Control Room(s), where possible. Rebalancing relates to the apportionment of curtailment/constraint across respective units (it does not change the extent of curtailment/constraint overall)
Pricing and imbalance settlement (based on DIs, PNs and metering)
No change to existing approach (although more instructions)

## Slide 20: Stakeholder Engagement: Industry Workshop
Trading & Settlement Code
Proposal submitted to Mods Committee ahead of scheduled Mods Committee Meeting
Grid Codes
Proposal submitted to Grid Code Review Panel (GCRP)/ Joint Grid Code Review Panel (JGCRP) ahead of scheduled GCRP/ JGCRP meetings
Proposal presented at Mods Committee Meeting
Final Recommendation Report submitted by Mods Committee to RAs
RA approval
Proposal presented at GCRP/ JGCRP meetings
Proposal submitted by TSO to RAs
RA approval
Public consultation following GCRP/ JGCRP meetings (NI only)
Updated T&SC published
Updated Grid Codes published
Code Change Process

## Slide 21: Stakeholder Engagement: Industry Workshop
Initiative | T&SC Mods Committee | Grid Code Review Panel/ Joint Grid Code Review Panel
SDP_02 – ESPS Integration | 19/10/2023 | 30/11/2023
SDP_01 – Operation of Non-Priority Dispatch of Renewables and SDP_04 – Wind/Solar Dispatchability Improvements | Feb 2024 (TBC) | Feb 2024 (TBC)
Code Change Schedule

## Slide 22: Stakeholder Engagement: Industry Workshop
Trading & Settlement Code
Registration – Will be required to register under a trading site
Data submission changes – Updates to registration data, COD (including forecasts), TOD
Grid Codes
Data submission changes
Minor text updates for clarification
Settlement changes - Decoupling from treatment of pumped storage, handling negative values, using Min Output as floor for inc QBOA calculations
Description of Changes for SDP_002: Energy Storage Power Stations

## Slide 23
  Stakeholder Engagement will continue. We will host more industry-wide workshops and focused sessions for different groups (technical, programme management).
  Engagement is bi-directional. We need to hear from you! You will hear from us.
  Ongoing bilateral meetings to discuss SDP details.
Stakeholder Engagement
Bilateral Meetings
Stakeholder Engagement: Industry Workshop
Ongoing Stakeholder Engagement
  Monthly cadence for Industry workshops
  Standing placeholder at Market Operator User Group
Industry-Wide Engagement

## Slide 24
  We understand the importance of meeting with 3rd party technology vendors – those that supply the tools, data, and reports for market participants.
  To date, we have met with one, are scheduled to speak with another, and are scheduling for a third meeting next week.
  Hitachi Energy nMarket
  BRADY EDIL, Market System
  EnAppSys (Reporting, Analytics)
Meeting with Technology Vendors
Who We Know
Stakeholder Engagement: Industry Workshop
Meeting with Technology Vendors
  Other vendors are looking to offer solutions into the SEM. We are fielding questions from them and will keep you informed of any additional contacts.
Other Vendors

## Slide 25
To raise an issue or query for the Scheduling & Dispatch Programme:
Stakeholder Engagement: Industry Workshop
Contacting SDP
Contact
SDP Queries
SchedulingandDispatch@Eirgrid.com
Operating Hours
9:00am - 5:00pm IPT (Mon-Fri)
Queries received outside of operating hours will be addressed the next business day.
Information to Provide
Your Name
Your email & phone number
Your organisation
Topic of Issue/Query
Description of the issue or query
Any additional information to aid in understanding the issue or query

## Slide 26
Stakeholder Engagement: Industry Workshop
Systems Delivery Update – SDP Tranche 1
PHASE 1
Analysis & Planning
PHASE 2
Detailed Requirements & Design
PHASE 3: Implementation
PHASE 4: Readiness and Rollout
PHASE 5
Support
System Delivery Phase Timeline / Milestones
System Delivery Milestones
Today
Solution Pathways identified & High Level Requirements
Detailed Requirements Definition completed
Final Design Specifications produced
System Build commences
Vendor Unit Test / FAT
Vendor delivery of code to EirGrid
System Test / E2E / User Acceptance Test
Post Go-Live Hypercare period
SDP Initiative – Tranche #1
SDP_01: Treatment of Non-Priority Dispatch Renewables
SDP_02: Energy Storage Power Stations
SDP_04: Wind Dispatch Improvement
294 Detailed Requirements
3 Core Operations Platforms
(Up to 11 downstream systems)
22 New / Updated Interfaces
Implementation and Go-Live for SDP Tranche 1

## Slide 27
  Please provide feedback when you have reviewed and considered the information from today’s discussion.
  Follow-up from any “Listen” item discussed today.
  Be on the lookout for the next Industry Workshop, to be scheduled at a monthly cadence.
Next Steps
Stakeholder Engagement: Industry Workshop
Next Steps

## Slide 28
Stakeholder Engagement: Industry Workshop
Actions and Open Questions

## Slide 29: SDP: Glossary
Term | Definition
BA | Business Analyst
BM | Balancing Market
CC | Control Centre
CCT | Control Centre Tools (LSAT, RMT & VTT)
COD | Commercial Offer Data
CSB | Counterparty Settlement and Billing
DI | Dispatch Instruction
DRDQ | Dispatch Regime Dispatch Quotient
EG | EirGrid / SONI / SEMO
EMS | Energy Management System
ESPS | Energy Storage Power Station
FFR | Fast Frequency Response
GDX | Group Data Exchange
GSP | Generator Setpoint
HIS | Historical Information Server
HLR | High Level Requirements
IPO | Innovation and Planning Office
IPQBOA | Instruction Profile Quantity Bid Offer Acceptance
JAPR | Jurisdictional Active Power Ratio
MI-STL | MMS to CSB integration
MMS | Market Management System
MOL | Merit Order List
MPI | Market Participant Interface
NF | Non-Functional
NPDR | Non-Priority Dispatch of Renewables Unit
OMS | Outage Management System
Term | Definition
OUI | Operator User Interface
PD RES | Priority Dispatch. Renewable Energy Source
PIMB | Imbalance Price Calculation
PIO | People and Information Office (IT)
PN | Physical Notification
PS | Pumped Storage
QD | Dispatch Quantity
QM | Metered Quantity
RMT | Ramping Margin Tool
ROM | Rough Order of Magnitude
RSD | Reserve Scheduling Dispatch
RT | Real Time
RTQBOA | Real Time Quantity Bid Offer Acceptance
RTU | Remote Terminal Unit
S&D | Scheduling and Dispatch
SCADA | Supervisory Control and Data Acquisition
SDP | Scheduling and Dispatch Programme
SEMO | Single Electricity Market Operator
SME | Subject Matter Expert
TOD | Technical Offer Data
TSO CSB | Transmission System Operator Counterparty Settlements & Billing
UC | Use Case
WDT | Wind Dispatch Tool
WEF | Wind Energy Forecast
WPRED | Wind Predictor