## Slide 1
September 2019
Scheduling & Dispatch

## Slide 2
COPYRIGHT NOTICE
All rights reserved. This entire publication is subject to the laws of copyright. This publication is confidential and sole property of EirGrid plc and SONI Limited. No part of this publication may be reproduced or transmitted in any form or by any means, electronic or manual, including photocopying without the prior written permission of EirGrid plc and SONI Limited. © SONI Limited / EirGrid Plc 2019
DOCUMENT DISCLAIMER
This manual is intended as a guide only. Whilst every effort is made to provide information that is useful, and care is taken in the preparation of the information, EirGrid plc and SONI limited give no warranties or representations, expressed or implied, of any kind with respect to the contents of this document, including, without limitation, its quality, accuracy and completeness. EirGrid plc and SONI limited hereby exclude, to the fullest extent permitted by law, all and any liability for any loss or damage howsoever arising from the use of this document or any reliance on the information it contains. Use of this document and the information it contains is at the user’s sole risk.

## Slide 3: Agenda
Introduction
Scheduling Process
Dispatch Process
WSAT

## Slide 4: Control Centre
Control Centres
Transmission
Generation
NCC Tx
Dublin
CHCC Tx
Belfast
Scheduling
Dispatch
NCC
Dublin
CHCC
Belfast
Rotates every 4 days
Notes: Key Duties Transmission Engineer:
Voltage Control at 400 kV, 220 kV and 110 kV
Monitoring MVA flow on power lines:
  Re-dispatch generators
  Sectionalise stations if necessary
Remote Control Operations & Live Switching
Contingency and Alarm Monitoring
Transmission Outage Management
Restoration of plant following disconnection

## Slide 5: From SEM to I-SEM
 | SEM | I-SEM
Gate closure | EA2 WD1 > 10 hr notice | Half-hourly 1 hr before real-time 08:40 11:54 18:10 ICRP updates
Unit Prices | Single curve Bidding Code of Practice ‘BCoP’ | Dual curve - Inc/Dec Simple and complex data Partly ‘BCoP’d
Start point for scheduling | Market prices (fixed), Interconnector nominations Current dispatch | Market Physical Notifications (PNs), Varying prices (from PNs), Interconnector schedules Current dispatch
Cost optimisation objective | Minimise production cost | Minimise cost of deviating from PNs*
Scheduling process | Day Ahead, Inday 1, Inday 2 & Inday 3, and ad hoc as required | Continuous (100+) Economic dispatch (every 5 mins)
Energy Balance | Implicitly balanced | Market participants are balance responsible
Price | Ex-post unconstrained price | Real Time Imbalance Price
*plus a number of additional objectives

## Slide 6: System Overview for Scheduling & Dispatch
Constraint/Curtailment Setpoints
  MMS
EDIL
DIs
MDMN MNMW SSRes
Declarations
Runs
Schedulers
Resource Dispatch
Online/Offline Merit Orders
DIs
EMS
Market Participant Interface
Imbalance Pricing
Network System Model
State
Estimator
Constraints
Load Forecast
Wind Forecast
Actual Demand
RT Availability
Actual Output
Tx Outages
Transmission Constraints
Reserve Curves
Interconnector Flow
COD
TOD
Physical Notifications
Station
Network
Model
Wind DIs
Declarations
Control Centre
Wind Setpoints
DIs
WSAT

## Slide 7
Scheduling
Scheduling

## Slide 8: Scheduling Run Sequence
Notes: Scheduling is the process of planning the dispatch instructions to be issued.
Given the time it takes for units to respond (start-up, shut-down and change output) can range from seconds to many hours, our scheduling process operates over a range of timescales:
  Real-Time Dispatch (RTD) – for the next hour
  Real-Time Commitment (RTC) – for the next four hours
  Long-Term Schedule (LTS) – for the next day

## Slide 9: The Optimisation
Minimise cost of
deviation from PNs
Operational Security Limit Violations
Priority Dispatch Curtailment
Increasing Optimisation Cost
Avoiding:
Objective:
Mechanism:
Constraint Violation Costs
Negative Decremental Prices

## Slide 10: Load Forecasting
Load Forecasting Model
Weather Data
Historical Load shapes
Special Days
Actual System Demand
Load Shapes
MMS
Schedulers
Load Predictor and Blending

## Slide 11: Load Prediction & Blending
Actual Demand
30min Long Term
Forecast
t (current time)
t + 4 hours
Schedulers Forecast
Blending Period
Long Term EMS Forecast
t + 2 hours
Load Shape
1 min Interpolated Forecast

## Slide 12: Load shapes
Chart: 
MW

## Slide 13: Wind Forecast
Schedulers
Wind Forecast
(every 6 hours)
RT Wind Availability
(every 5 min)
MMS
Runs every minute, blending real-time availability to wind forecasts.
Capability to weight or average forecasts to produce a single forecast for use in scheduling

## Slide 14: Wind Forecast Blending
Wind Forecast
t (current time)
t + 2 hours
Schedulers Forecast
Blending Period
Long Term Forecast
Actual Wind Availability (or if non existent then Actual Output)

## Slide 15: Actual Wind v’s Forecast Wind
Chart: 

## Slide 16: Commercial Offer Data (COD)
The following Bid Offer Data is used in each run type for scheduling decisions:
Scheduling/Dispatch Run | Source of Commercial Data |  | 
 | Primary | Back-Up 1 | Back-Up 2
LTS – Long Term Schedule | Complex | Default | N/A
RTC – Real-Time Commitment | Complex | Default | N/A
RTD – Real-Time Dispatch | Simple | Complex | Default
SUC
H
No Load Costs
SUC
W
SUC
C
Inc 1
Dec 1
Inc 2
Dec 2
Inc 10
Dec 10
COMPLEX
Inc 1
Dec 1
Inc 2
Dec 2
Inc 10
Dec 10
SIMPLE

## Slide 17: Cost Curve
Production of Composite Cost Curves:
Incremental Offer Curve
Decremental Bid Curve
Price
Quantity
PN
Composite Curve

## Slide 18: Technical Offer Data (TOD)
As detailed in Appendix I of Trading and Settlement Code, largely unchanged from SEM including:
  Block load
  Load up rate
  Soak up time
  Minimum Stable Generation level
  Ramp up rate
  Dwell up time
  Ramp down rate
  Dwell down time
  Maximum Availability
  Minimum On Times, Minimum Off Time
  Cooling Boundaries
  Forecast Profiles (Availability, Minimum Output, Minimum Stable Generation)
  Short-term Maximisation Capacity and Time
  Synchronous Start up times for three different heat states
  De-load rate

## Slide 19: Reserve
Reserve MW
Unit Output MW
Primary Operating Reserve (POR) Curve
0
R1
R2
GMX
GMX-∆1
∆1
GMN
β
GMN+β
GMN | 140
GMX | 400
R1 | 15
R2 | 25
β | 60
∆1 | 25
Primary Operating Reserve (POR) – 5 to 15 Seconds
Secondary Operating Reserve (SOR) – 15 to 90 Seconds
Tertiary Operating Reserve 1 (TOR1) – 90 to 5 Minutes
Tertiary Operating Reserve 2 (TOR2) – 5 to 20 Minutes
Required to carry
75% Largest Infeed
Required to carry
100% Largest Infeed

## Slide 20: Interconnector Reference Program
Ex-ante Market Interconnector Schedule
Interconnector Flow (MW)
Trading Period
Interconnector Reference Program
Production of Interconnector Reference Programme:

## Slide 21: Example PN’s
PNs | Availability Max / Min | 08:00 | 09:00 | 10:00 | 11:00 | 12:00 | 13:00 | 14:00 | 15:00 | 16:00 | 17:00 | 18:00 | 19:00 | 20:00 | 21:00
Unit A | 400 / 200 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400
Unit B | 400 / 200 | 300 | 350 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 300 | 200
Unit C | 400 / 200 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Unit D | 300 / 100 | 100 | 200 | 250 | 250 | 300 | 250 | 200 | 200 | 200 | 250 | 300 | 300 | 250 | 200
Unit E | 300 / 100 | 100 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 250 | 300 | 200 | 100 | 100
Unit F | 100 / 20 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 100 | 100 | 50 | 0 | 0
Unit G | 100 / 20 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 50 | 0 | 0 | 0
Unit H | 50 / 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Total PN |  | 900 | 1150 | 1250 | 1250 | 1300 | 1250 | 1200 | 1200 | 1200 | 1400 | 1550 | 1350 | 1050 | 900
Demand |  | 900 | 1150 | 1250 | 1250 | 1300 | 1250 | 1200 | 1200 | 1200 | 1400 | 1550 | 1350 | 1050 | 900
Snapshot of PNs submitted for 08:00 to 21:00
For illustration purposes this data is presented at hourly resolution.

## Slide 22: Example PN’s
time
MW

## Slide 23: System Security
Reserve |  | Thermal |  | Voltage |  | Dynamic Stability |  | Short Circuit
(Frequency) |  |  |  |  |  |  |  | 
All Island OR Requirement |  | North-South Tie-Line Limit |  | NI North West Generation |  | Inertia |  | Operational Switching
NI/ROI Min OR Requirement |  | Cork Generation Export Limit |  | Dublin Generation |  | RoCoF |  | 
NI/ROI Replacement Reserve ("GTs") |  |  |  | South West Must Run |  | SNSP |  | 
NI/ROI Negative Ramping Reserve |  |  |  | 400kV network Generation |  | NI 3 Units Must Run |  | 
Ramping (1hr 3hr 8hr) |  |  |  |  |  | ROI 5 Units Must Run |  | 

## Slide 24: LTS Example
PNs | Availability Max / Min | 08:00 | 09:00 | 10:00 | 11:00 | 12:00 | 13:00 | 14:00 | 15:00 | 16:00 | 17:00 | 18:00 | 19:00 | 20:00 | 21:00
Unit A | 400 / 200 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400
Unit B | 400 / 200 | 300 | 350 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 400 | 300 | 200
Unit C | 400 / 200 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Unit D | 300 / 100 | 100 | 200 | 250 | 250 | 300 | 250 | 200 | 200 | 200 | 250 | 300 | 300 | 250 | 200
Unit E | 300 / 100 | 100 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 250 | 300 | 200 | 100 | 100
Unit F | 100 / 20 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 100 | 100 | 50 | 0 | 0
Unit G | 100 / 20 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 50 | 0 | 0 | 0
Unit H | 50 / 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Total PN |  | 900 | 1150 | 1250 | 1250 | 1300 | 1250 | 1200 | 1200 | 1200 | 1400 | 1550 | 1350 | 1050 | 900
Demand |  | 900 | 1150 | 1250 | 1250 | 1300 | 1250 | 1200 | 1200 | 1200 | 1400 | 1550 | 1350 | 1050 | 900
Schedule | Availability Max / Min | 08:00 | 09:00 | 10:00 | 11:00 | 12:00 | 13:00 | 14:00 | 15:00 | 16:00 | 17:00 | 18:00 | 19:00 | 20:00 | 21:00
Unit A | 400 / 200 | 370 | 370 | 370 | 370 | 370 | 370 | 370 | 370 | 370 | 370 | 370 | 370 | 370 | 370
Unit B | 400 / 200 | 330 | 350 | 370 | 370 | 370 | 370 | 370 | 370 | 370 | 370 | 370 | 370 | 280 | 230
Unit C | 400 / 200 | 0 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 0
Unit D | 300 / 100 | 100 | 130 | 210 | 210 | 260 | 210 | 160 | 160 | 160 | 250 | 270 | 270 | 100 | 200
Unit E | 300 / 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 190 | 270 | 120 | 100 | 100
Unit F | 100 / 20 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 20 | 20 | 20 | 0 | 0
Unit G | 100 / 20 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 50 | 0 | 0 | 0
Unit H | 50 / 10 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Total Sch |  | 900 | 1150 | 1250 | 1250 | 1300 | 1250 | 1200 | 1200 | 1200 | 1400 | 1550 | 1350 | 1050 | 900
Demand |  | 900 | 1150 | 1250 | 1250 | 1300 | 1250 | 1200 | 1200 | 1200 | 1400 | 1550 | 1350 | 1050 | 900
LTS Run
Notes: At 18:00 LTS pulls back the units from their PN’s for reserve and system constraints

## Slide 25: LTS Example Cont’d
time
MW
Unit C Dispatched to meet demand
1350MW of total PN’s Scheduled following LTS run
200MW short
Scheduled with PN
Scheduled without PN

## Slide 26: Forecast Availability v Declared
 | Declared Max [MW] | Forecast Avail Max [MW]
Unit A | 400 | 425
Unit B | 400 | 408
Unit C | 400 | 435
Unit D | 300 | 310
Unit E | 300 | 308
Unit F | 100 | 105
Unit G | 100 | 110
Unit H | 50 | 59
 | 2050 | 2160
110MW Difference
LTS Availability
time
MW
Scheduled with PN
Scheduled without PN
Real time scheduled
In Real Time expensive short notice plant called to fill the gap.
LTS uses forecast availability, when it comes to real time the declared availability can be much lower, this leaves the real time schedules short, causing expensive short notice plant to be called, affecting imbalance pricing.

## Slide 27
Scheduling
Dispatch

## Slide 28: Dispatch
Unit | Current DI | Min Gen | Max Gen | Actual Output | PN | Price € MWh
A | 396 | 150 | 431 | 398 | 431 | 20
B | 335 | 130 | 390 | 332 | 380 | 25
C | 375 | 100 | 400 | 374 | 400 | 26
D | 60 | 20 | 120 | 60 | 100 | 30
INC/DEC Merit Order
Unit | PN | Min Gen | Max Gen | Cost € MWh | Notification Time [hr]
E | 0 | 10 | 55 | 80 | 0.17
F | 0 | 10 | 50 | 120 | 0.33
G | 0 | 20 | 90 | 125 | 0.33
H | 0 | 60 | 250 | 20,000 | 6
OFFLINE Merit Order
EDIL
Control Room
Gen Station

## Slide 29: Wind Dispatch
Active Power Control Status
Transfers control of active power setpoint to TSO control centre
Available MW
Calculated value provided by the wind farm
Wind MW
Present wind farm output
WF Setpoint
Active MW setpoint wind farm controller
Reason for Wind dispatch
Curtailment required for high wind output at low loads and minimum generation.
Constraint required if there is insufficient transmission capacity to transport wind generation from weakly
connected regions.
Curtailment/Constraint setpoints are issued to windfarms via the wind dispatch tool in the EMS

## Slide 30
Scheduling
WSAT

## Slide 31: Power System Stability
Transient stability: the ability of the power system and individual generators to maintain synchronism after an operational disturbance. The system is within the stability limit when, after some given fault situations, it is able to return to an acceptable steady state situation.
20 s
5 mins
TSAT- transient period; automatic measures operate
VSAT – quasi steady state; time period before manual actions
Notes: Voltage stability in the power system is defined as the ability of a power system to maintain acceptable voltages at all buses in the system under normal conditions and after being subjected to a disturbance.
Frequency stability is the ability of the power system to maintain steady state frequency, following a severe system disturbance, resulting in a significant imbalance between generation and load.

## Slide 32: WSAT (Wind Security Assessment Tool)
Developed by EirGrid and external company to monitor the stability of the Irish power system with increasing levels of wind generation.
Determines the voltage and transient stability of the system calculated for fault and no-fault conditions.
WSAT
EMS
List of
preventative measures
Control Room acts
EDIL
VSAT
TSAT
Runs every 5 minutes

## Slide 33: What affects Transient Stability?
Network Short-Circuit Level
The higher the SCMVA, the more stable a machine
SCMVA related to how many machines in vicinity and
the state of the network how many outages
Machine MW Output
Within an operational range the higher the MW, the
less stable a machine
Machine MVAr Output
Absorbing MVArs BAD, Producing MVArs GOOD
To do with strength of the field between stator and rotor
Machine Terminal Voltage
Higher is better
Number of Synchronised Machines
# of machines is better
Synchronised
Machines
Stability

## Slide 34: WSAT Example (Loss of North – South Tie Line)
Import 420MW
Import 500MW
300MW N-S
Largest Single Infeed 500MW
POR Required 75% of 500MW = 375MW
North – South flow = 300MW, (Limit 450MW – 20MW Offset)
NI POR = 130MW
300+Min(130, 500 - 0.25*250) ≤ 430
430 = S_MWR_NI = Max Flow
ROI POR = 250MW
N-S Net Flow (Scheduled flow + Reserve)

## Slide 35: WSAT Example (Loss of North – South Tie Line)
Time (sec)
Frequency (Hz)
50.04
48.85
UFLS Trigger frequency
For loss of Tie Line
System Separation
Low Frequency in ROI, UFLS triggered.
ROI system low inertia, only 5 big generators ON.
Frequency slow to recover.
High Frequency in NI.
Interconnector runback activated and recovers NI frequency to within limits.
Preventative Control Measures
Reduce the Tie Line flow by decreasing Generation in NI (reduce generation, reduce Moyle import or Constrain wind)
Increase reserve provision in ROI, re-dispatch out of merit generation.
Sync additional generation.
NI System frequency
ROI System frequency

## Slide 36: System Overview for Scheduling & Dispatch
Constraint/Curtailment Setpoints
  MMS
EDIL
DIs
MDMN MNMW SSRes
Declarations
Runs
Schedulers
Resource Dispatch
Online/Offline Merit Orders
DIs
EMS
Market Participant Interface
Imbalance Pricing
Network System Model
State
Estimator
Constraints
Load Forecast
Wind Forecast
Actual Demand
RT Availability
Actual Output
Tx Outages
Transmission Constraints
Reserve Curves
Interconnector Flow
COD
TOD
Physical Notifications
Station
Network
Model
Wind DIs
Declarations
Control Centre
Wind Setpoints
DIs
WSAT