## Slide 1: Impact Assessment Mod_11_12 : Proposal to extend the definition of Special Units to include Compressed Air Energy Storage 23 January 2013
Notes: *
*
<number>##

## Slide 2
Modification: Proposal by Gaelectric Energy Storage Ltd. to designate Compressed Air Energy Storage as a Special Unit in the Code as develop market rules for it on that basis
  Two options were put forward for Impact Assessment purposes
    Option 1(a): Pumped Storage Unit with Commercial Offer Data
    Option 1(b): Pumped Storage Unit with Commercial Offer Data and a Pumped Storage Cycle Efficiency which is a function of output rather than constant
    Option 2: New Unit with similar logic to Interconnector Units
Impact Assessment of Mod_11_12
Notes: <number>

## Slide 3
SEMO developed a change request and discussed the options with the vendor in a number of conference calls
  Option 2 was discussed at length, but the vendor did not feel that it would fit well into the existing system architecture. Their view was as follows:
  In the existing implementation, Interconnector units’ bid/offer capacity are limited by capacity holdings. CAES would not have a similar capacity holding mechanism. Therefore, it would not consider the physical limits of CAES in the UUC optimisation. Instead, the physical limits would be imposed by post-processing, modifying the market schedule quantities (MSQs) determined by the UUC. This post processing would cause sub-optimal solutions for MSQ and SMP and would in turn introduce unfair competition into SEM.
  Based on this, it was decided not to proceed further with Option 2 and to perform a detailed impact assessment of Option 1(a) and 1(b)
Impact Assessment development
Notes: <number>

## Slide 4
  Option 1(a):
  New CAES unit which replicates all existing of existing PS unit
  In addition includes complex COD (Start Up Costs, No Load Costs and PQ pairs)
  Energy Payments, Constraint Payments, Uninstructed Imbalance Payments and Make Whole Payments would use the formulae for PPMGs
  Capacity Payments would the formulae for PS units except for the calculation of CPGPF where the PPMG formulae would be used
Vendor Impact Assessment
Notes: <number>

## Slide 5
  Option 1(a) System Changes:
    Changes to MA :
      MA input
      SMP calculation
    Changes to MI :
      MPR
      Validations
      Database
      MI-MOI GUI
    Settlement changes
  Option 1(a) Cost: €222,000 (ABB) + €155,230 = € 377,230 + Testing
Vendor Impact Assessment
Notes: <number>

## Slide 6
  Option 1(b):
  Functionality as in Option 1(a)
  In addition, Pumped Storage Cycle Efficiency (PSCE) would be changed from a constant to a function that varies with the output of the unit (piecewise linear function).
Vendor Impact Assessment (cont’d)
Notes: <number>

## Slide 7
  Option 1(b) System Changes:
    Changes to MA :
      MA input
      SMP calculation
      PSCE function and min/max charging including display changes
      PSCE function model in LR
      PSCE function model in MIP
    Changes to MI :
      MPR
      Validations
      Database
      MI-MOI GUI
    Settlement changes
  Option 1(b) Cost: € 222,000 + €448,000 (ABB) + €155,230 =
  € 825,230 + Testing
Vendor Impact Assessment
Notes: <number>

## Slide 8
    Changes assessed only apply to Central Market Systems
    RCUC would also need to be changed accordingly
    Assessment for this, if required would be additional
Next Steps
Notes: <number>