## Slide 1: INTRA-DAY TRADING DESIGN Functional Group 2: Other Data Transactions, MSP Software Operation, Reports and Publications, Required Credit Cover Query 27 September 2011
Notes: *
*
<number>##

## Slide 2
Contents
Introduction
EA1 MSP Software Runs
EA2 MSP Software Runs
WD1 MSP Software Runs
EP1 MSP Software Runs
EP2 MSP Software Runs
MSP Software Run Cancellation
Treatment of Energy Limited Units
Other Data Transactions
Publications & Reports
Required Credit Cover Query
Glossary
Notes: <number>

## Slide 3
Contents
Introduction
EA1 MSP Software Runs
EA2 MSP Software Runs
WD1 MSP Software Runs
EP1 MSP Software Runs
EP2 MSP Software Runs
MSP Software Run Cancellation
Treatment of Energy Limited Units
Other Data Transactions
Publications & Reports
Required Credit Cover Query
Glossary
Notes: <number>

## Slide 4
Operation of the MSP Software (for each Run):
  Initial Conditions
  Commercial Offer Data
  Technical Offer Data
  Contingency Data
  Calculation of Schedule Demand
  Interconnector/Interconnector Unit Constraints
  MSP Software Run Cancellation
Other Data Transactions (not submitted by Participants):
  System Operators to Market Operator
  Interconnector Administrators to Market Operator
  Market Operator to System Operators
  Market Operator to Interconnector Administrators
Reports and Publications
Required Credit Cover Query
Scope of Functional Group 2
Notes: <number>

## Slide 5
Contents
Introduction
EA1 MSP Software Runs
EA2 MSP Software Runs
WD1 MSP Software Runs
EP1 MSP Software Runs
EP2 MSP Software Runs
MSP Software Run Cancellation
Treatment of Energy Limited Units
Other Data Transactions
Publications & Reports
Required Credit Cover Query
Glossary
Notes: <number>

## Slide 6
Recap: SEM Intra-Day Trading Design
Start Overlap
Opt’n Period
Trading Day - 1
Trading Day
Gate Window
Closure
(GWC)
EA1
Gate Window
Opening
(GWO)
e.g. as per current
GWC
EA2
GWO
GWC
WD1
GWO
GATE WINDOW
10:00 TD-29 to 09:30 TD-1
GATE WINDOW
09:30 TD-1 to 11:30 TD-1
GATE WINDOW
11:30 TD-1 to 08:00 TD
EA1 Trading Window
EA2 Trading Window
WD1 Trading
Window
Ending Overlap
Opt’n Period
Ending Overlap
Opt’n Period
Ending Overlap
Opt’n Period
Latest EA1 Interconnector Unit trades fixed
Latest EA1 and EA2 Interconnector Unit trades fixed
OPTIMISATION TIME HORIZON
Notes: Key points:
All can bid to each Gate (other than non Capacity Holders in EA1).
As per EU guidelines, EA2 is the opportunity reallocate Interconnector capacity on D-1 and WD1 is the opportunity to reallocate on D.
<number>

## Slide 7
Each MSP Software Run needs Initial Conditions at the start of the Optimisation Time Horizon:
  Initial Status (ON or OFF)
  Initial MW (MSQ from last Trading Period in the previous Trading Day).
  Last Status Change Date/Time
  First Available Time
  Start Up Cost Carried over
  Start Up Time Hot/Warm/Cold
For EA1, the Initial Conditions will be taken from the latest WD1 ,EA2 or EA1 MSP Software Run that covered the end of the Trading Day.
EA1 – Initial Conditions
Trading Day D-1
Trading Day D
Ending Overlap
Optimisation Period
Initial
Conditions
Ending Overlap
Optimisation Period
Priority order for Initial Conditions (1 to 3):
1. If WD1 MSP Software Run completed for Trading Day D-1, Initial Conditions from WD1
2. If EA2 MSP Software Run completed for Trading Day D-1, Initial Conditions from EA2
3. If EA1 MSP Software Run completed for Trading Day D-1, Initial Conditions from EA1
Notes: <number>

## Slide 8
Note:
Interconnector Units do not have Default Data and will not be included within the market schedule where COD is not Accepted.
EA1 – Commercial Offer Data
Trading Day D
Ending Overlap
Optimisation Period
EA1 Gate Window
Commercial Offer Data
Price Quantity Pairs
No Load Costs
Start Up Costs
Shut Down Costs
Decremental Price
Maximum Interconnector Unit Import Capacity
Maximum Interconnector Unit Export Capacity
GWO
10:00 TD-29
GWC
09:30 TD-1
Calculate Offered Modified PQ Pairs for Interconnector Units with Accepted EA1 COD (for Interconnector Units, Offered Modified PQ pairs are the EA1 COD).
If no Accepted EA1 COD, use Starting Gate Window Data = Default Data.
COD for entire Optimisation Time Horizon
EA1 Trading Window
Notes: <number>

## Slide 9
EA1 – Technical Offer Data
Trading Day D
Ending Overlap
Optimisation Period
EA1 Gate Window
Technical Offer Data
VTOD Set Selection (10 mins prior to GWC)
Forecast Avail, MSG, MINOUT
Other Technical Offer Data
GWO
10:00 TD-29
GWC
09:30 TD-1
If no Accepted EA1 TOD, use Starting Gate Window Data = Default Data.
EA1 Trading Window
Latest Accepted and Utilised TOD for each Trading Period (EA1)
Notes: <number>

## Slide 10
The MSP Software pre-processor will identify when sufficient data is not available and Contingency Data needs to be used.
The Contingency Data is always based on the latest Accepted data.
EA1 Contingency Data (HLD section 3.5.4)
Data Transaction | EA1 Contingency Data
Four Day Load Forecast | Most recent Four Day Load Forecast Accepted by the relevant Gate Window Closure
Wind Power Unit Forecast | Most recent Wind Forecast Accepted by the relevant Gate Window Closure
Interconnector Available Transfer Capacity | Most recent ATC data Accepted by the relevant Gate Window Closure
Active Interconnector Capacity Holdings | Auction Platform will provide the data prior to the EA1 Gate Window Closure. If not received via the CMS, data shall be faxed and emailed by the IA to SEMO. If not received from the IA by any means, zeros will be used.
Load Forecast is submitted each day for at least the following four Calendar Days.
Wind Forecast is submitted once prior to the EA1 Gate Window Closure and as updated
IA for Moyle/EWIC planning to submit Active Capacity Holdings on D-1, immediately post day ahead auctions.
ATC is submitted each day for the following Trading Day and associated Ending Overlap Optimisation Period.
Notes: <number>

## Slide 11
No change from the current calculation.
Will utilise Accepted COD/TOD by the EA1 Gate Window Closure.
For External Data Providers (e.g. TSOs), latest data received will be used (or Contingency Data, if required).
EA1 – Calculation of Schedule Demand
Demand Forecast
(A)
Nominated
Quantity
(B)
Forecast
Availability
Wind
Forecast
MINUS
MIN(A,B)
Affected Units
Demand Forecast, net of Autonomous Non-Wind
PPTG Non-Wind,
VPTG Non-Wind,
PPMG Under Test Non-Wind,
VPMG Under Test Non-Wind
(A)
Wind
Forecast
(B)
Forecast
Availability
MIN(A,B)
VPTG Wind,
VPMG Under Test Wind
MINUS
MINUS
Data Source
Autonomous Wind
System Operators
Participants via COD/TOD submitted by EA1 Gate Window Closure
Forecast Availability via TOD submitted by EA1 Gate Window Closure
Wind Forecast from System Operators
System Operators
Calculation
Notes: <number>

## Slide 12
The Interconnector Ramp Rate will continue to be applied in the Ex-Ante One MSP Software Run.
The same constraints for Interconnector Units will be applied in the Ex-Ante One Market Schedule as currently:
EA1 – Interconnector/Interconnector Unit Constraints
Price
Quantity (MW)
Lower
Operating
Limit *
Higher
Operating
Limit
Range within which the MSQ (=IUN) may be optimised by the MSP Software
Where:
AECH Active Export Capacity Holding
AICH Active Import Capacity Holding
MIUEC Maximum Interconnector Unit Export Capacity
MIUIC Maximum Interconnector Unit Import Capacity
* May be set to zero where PQ Pairs have been excluded as part of the calculation of Offered Modified PQ Pairs (Appendix P)
Notes: <number>

## Slide 13
EA1 Gate Window Closure 09:30
Notes: Key points:
All can bid to each Gate (other than non Capacity Holders in EA1).
As per EU guidelines, EA2 is the opportunity reallocate Interconnector capacity on D-1 and WD1 is the opportunity to reallocate on D.
<number>

## Slide 14
EA1 MSP Software Run by 11:00
Notes: Key points:
All can bid to each Gate (other than non Capacity Holders in EA1).
As per EU guidelines, EA2 is the opportunity reallocate Interconnector capacity on D-1 and WD1 is the opportunity to reallocate on D.
<number>

## Slide 15
Contents
Introduction
EA1 MSP Software Runs
EA2 MSP Software Runs
WD1 MSP Software Runs
EP1 MSP Software Runs
EP2 MSP Software Runs
MSP Software Run Cancellation
Treatment of Energy Limited Units
Other Data Transactions
Publications & Reports
Required Credit Cover Query
Glossary
Notes: <number>

## Slide 16
Recap: SEM Intra-Day Trading Design
Start Overlap
Opt’n Period
Trading Day - 1
Trading Day
Gate Window
Closure
(GWC)
EA1
Gate Window
Opening
(GWO)
e.g. as per current
GWC
EA2
GWO
GWC
WD1
GWO
GATE WINDOW
10:00 TD-29 to 09:30 TD-1
GATE WINDOW
09:30 TD-1 to 11:30 TD-1
GATE WINDOW
11:30 TD-1 to 08:00 TD
EA1 Trading Window
EA2 Trading Window
WD1 Trading
Window
Ending Overlap
Opt’n Period
Ending Overlap
Opt’n Period
Ending Overlap
Opt’n Period
OPTIMISATION TIME HORIZON
Latest EA1 Interconnector Unit trades fixed
Latest EA1 and EA2 Interconnector Unit trades fixed
Notes: Key points:
All can bid to each Gate (other than non Capacity Holders in EA1).
As per EU guidelines, EA2 is the opportunity reallocate Interconnector capacity on D-1 and WD1 is the opportunity to reallocate on D.
<number>

## Slide 17
Each MSP Software Run needs Initial Conditions at the start of the Optimisation Time Horizon:
  Initial Status (ON or OFF)
  Initial MW (MSQ from last Trading Period in the previous Trading Day).
  Last Status Change Date/Time
  First Available Time
  Start Up Cost Carried over
  Start Up Time Hot/Warm/Cold
For EA2, the Initial Conditions will be taken from the latest WD1, EA2 or EA1
MSP Software Run that covered the end of the previous Trading Day.
EA2 – Initial Conditions
Trading Day D-1
Trading Day D
Ending Overlap
Optimisation Period
Initial
Conditions
Ending Overlap
Optimisation Period
Priority order for Initial Conditions (1 to 3):
1. If WD1 MSP Software Run completed for Trading Day D-1, Initial Conditions from WD1
2. If EA2 MSP Software Run completed for Trading Day D-1, Initial Conditions from EA2
3. If EA1 MSP Software Run completed for Trading Day D-1, Initial Conditions from EA1
Notes: <number>

## Slide 18
EA2 – Commercial Offer Data
Trading Day D
Ending Overlap
Optimisation Period
EA2 Gate Window
Commercial Offer Data
Price Quantity Pairs
No Load Costs
Start Up Costs
Shut Down Costs
Decremental Price
Maximum Interconnector Unit Import Capacity
Maximum Interconnector Unit Export Capacity
GWO
09:30 TD-1
GWC
11:30 TD-1
Calculate Offered Modified PQ Pairs for Interconnector Units with Accepted EA2 COD (for Interconnector Units, Offered Modified PQ pairs are the EA2 COD).
If no Accepted EA2 COD, use Starting Gate Window Data = Accepted EA1 COD, taking Default Data into account where applicable.
Latest MIUNs for EA1 Interconnector Unit are treated as fixed in the EA2 market schedule.
COD for entire Optimisation Time Horizon
EA2 Trading Window
Note:
Interconnector Units do not have Default Data and will not be included within the market schedule where COD is not Accepted.
Notes: <number>

## Slide 19
EA2 – Technical Offer Data
Trading Day D
Ending Overlap
Optimisation Period
EA2 Gate Window
GWO
09:30 TD-1
GWC
11:30 TD-1
EA2 Trading Window
Technical Offer Data
VTOD Set Selection (10 mins prior to GWC)
Forecast Avail, MSG, MINOUT
Other Technical Offer Data
If no Accepted EA2 Forecasts, Starting Gate Window Data = Default Data.
If no Accepted VTOD Set Selection, latest Accepted Data = EA1 Set Selection if Accepted, otherwise Default Data.
Other Technical Offer Data = Default Data
Latest Accepted and Utilised TOD for each Trading Period (EA2)
Notes: <number>

## Slide 20
EA2 Contingency Data (HLD section 3.5.4)
Data Transaction | EA2 Contingency Data
Four Day Load Forecast | Most recent Four Day Load Forecast Accepted by the relevant Gate Window Closure
Wind Power Unit Forecast | Most recent Wind Forecast Accepted by the relevant Gate Window Closure
Interconnector Available Transfer Capacity | Most recent ATC data Accepted by the relevant Gate Window Closure
Modified Interconnector Unit Nominations | IUNs if available from the EA1 MSP Software Run. If not, zeros will be used.
Load Forecast is submitted each day for at least the following four Calendar Days.
Wind Forecast is submitted once prior to the EA1 Gate Window Closure and as updated
ATC is submitted each day for the following Trading Day and associated Ending Overlap Optimisation Period.
IUNs should be available, as EA1 MSP Software Runs cannot be cancelled.
The MSP Software pre-processor will identify when sufficient data is not available and Contingency Data needs to be used.
The Contingency Data is always based on the latest Accepted data.
Notes: <number>

## Slide 21
No change from the current calculation.
Will utilise Accepted COD/TOD by the EA2 Gate Window Closure.
For External Data Providers (e.g. TSOs), latest data received will be used.
EA2 – Calculation of Schedule Demand
Demand Forecast
(A)
Nominated
Quantity
(B)
Forecast
Availability
Wind
Forecast
MINUS
MIN(A,B)
Affected Units
Demand Forecast, net of Autonomous Non-Wind
PPTG Non-Wind,
VPTG Non-Wind,
PPMG Under Test Non-Wind,
VPMG Under Test Non-Wind
(A)
Wind
Forecast
(B)
Forecast
Availability
MIN(A,B)
VPTG Wind,
VPMG Under Test Wind
MINUS
MINUS
Data Source
Autonomous Wind
System Operators
Participants via COD/TOD submitted by EA2 Gate Window Closure
Forecast Availability via TOD submitted by EA2 Gate Window Closure
Wind Forecast from System Operators
System Operators
Calculation
Notes: <number>

## Slide 22
For the EA2 MSP Software Run, Capacity Holdings are not required.
Any Interconnector User may trade via an Interconnector on which they have registered.
For Interconnectors as a whole, MSQs will be limited in aggregate by the Interconnector Ramp Rate and Interconnector Import and Export ATC, treating the EA1 MIUNs as fixed:
EA2 – Interconnector Constraints
The maximum export capacity for the Interconnector
MSQ for the Interconnector Unit that is optimised by the EA2 MSP Software Run
Latest MIUNs for the Units optimised by the EA1 MSP Software Run treated as fixed
The maximum import capacity for the Interconnector
Notes: <number>

## Slide 23
For Interconnector Units, Active Capacity Holdings are not required.
Instead, EA2 MSQs are only limited in accordance with the maximum import/export trades as submitted by the Participant in their Commercial Offer Data to the EA2 Gate Window:
EA2 – Interconnector Unit Constraints
Price
Quantity (MW)
Lower
Operating
Limit *
Higher
Operating
Limit
Range within which the MSQ may be
optimised by the MSP Software
Where:
MIUEC Maximum Interconnector Unit Export Capacity
MIUIC Maximum Interconnector Unit Import Capacity
* May be set to zero where PQ Pairs have been excluded as part of the calculation of Offered Modified PQ Pairs (Appendix P)
Notes: <number>

## Slide 24
EA2 Gate Window Closure 11:30
Notes: Key points:
All can bid to each Gate (other than non Capacity Holders in EA1).
As per EU guidelines, EA2 is the opportunity reallocate Interconnector capacity on D-1 and WD1 is the opportunity to reallocate on D.
<number>

## Slide 25
EA2 MSP Software Run by 13:00
Notes: Key points:
All can bid to each Gate (other than non Capacity Holders in EA1).
As per EU guidelines, EA2 is the opportunity reallocate Interconnector capacity on D-1 and WD1 is the opportunity to reallocate on D.
<number>

## Slide 26
Contents
Introduction
EA1 MSP Software Runs
EA2 MSP Software Runs
WD1 MSP Software Runs
EP1 MSP Software Runs
EP2 MSP Software Runs
MSP Software Run Cancellation
Treatment of Energy Limited Units
Other Data Transactions
Publications & Reports
Required Credit Cover Query
Glossary
Notes: <number>

## Slide 27
Recap: SEM Intra-Day Trading Design
Start Overlap
Opt’n Period
Trading Day - 1
Trading Day
Gate Window
Closure
(GWC)
EA1
Gate Window
Opening
(GWO)
e.g. as per current
GWC
EA2
GWO
GWC
WD1
GWO
GATE WINDOW
10:00 TD-29 to 09:30 TD-1
GATE WINDOW
09:30 TD-1 to 11:30 TD-1
GATE WINDOW
11:30 TD-1 to 08:00 TD
EA1 Trading Window
EA2 Trading Window
WD1 Trading
Window
Ending Overlap
Opt’n Period
Ending Overlap
Opt’n Period
Ending Overlap
Opt’n Period
OPTIMISATION TIME HORIZON
Latest EA1 Interconnector Unit trades fixed
Latest EA1 and EA2 Interconnector Unit trades fixed
Notes: Key points:
All can bid to each Gate (other than non Capacity Holders in EA1).
As per EU guidelines, EA2 is the opportunity reallocate Interconnector capacity on D-1 and WD1 is the opportunity to reallocate on D.
<number>

## Slide 28
Each MSP Software Run needs Initial Conditions at the start of the Optimisation Time Horizon:
  Initial Status (ON or OFF)
  Initial MW (MSQ from last Trading Period in the previous Trading Day).
  Last Status Change Date/Time
  First Available Time
  Start Up Cost Carried over
  Start Up Time Hot/Warm/Cold
For WD1, the Initial Conditions will be taken from the latest WD1, EA2 or EA1 MSP Software Run that covered the end of the previous Trading Day.
WD1 – Initial Conditions
Trading Day D-1
Trading Day D
Ending Overlap
Optimisation Period
Initial
Conditions
Ending Overlap
Optimisation Period
Priority order for Initial Conditions (1 to 3):
1. If WD1 MSP Software Run completed for Trading Day D-1, Initial Conditions from WD1
2. If EA2 MSP Software Run completed for Trading Day D-1, Initial Conditions from EA2
3. If EA1 MSP Software Run completed for Trading Day D-1, Initial Conditions from EA1
Notes: <number>

## Slide 29
WD1 – Commercial Offer Data
Trading Day D
Ending Overlap
Optimisation Period
WD1 Gate Window
Commercial Offer Data
Price Quantity Pairs
No Load Costs
Start Up Costs
Shut Down Costs
Decremental Price
Maximum Interconnector Unit Import Capacity
Maximum Interconnector Unit Export Capacity
GWO
11:30 TD-1
GWC
08:00 TD
Calculate Offered Modified PQ Pairs for Interconnector Units with Accepted WD1 COD (for Interconnector Units, Offered Modified PQ pairs are the WD1 COD)
For other Generator Units, in each Trading Period in the WD1 Trading Window:
  If no Accepted WD1 COD, use Starting Gate Window Data = latest Accepted and Utilised COD (Accepted EA2 COD if EA2 not Cancelled, otherwise Accepted EA1 COD, taking Default Data into account where applicable).
For other Generator Units, in each Trading Period in the “SOOP”:
  If no Accepted WD1 COD, Use Starting Gate Window Data = latest Accepted and Utilised COD (Accepted EA2 COD if EA2 not Cancelled, otherwise Accepted EA1 COD, taking Default Data into account where applicable).
Latest MIUNs for EA1 and EA2 Interconnector Units are treated as fixed in the WD1 market schedule.
WD1 Trading Window
Starting Overlap
Optimisation Period
Latest Accepted and Utilised COD for each Trading Period (EA2/WD1)
Note:
Interconnector Units do not have Default Data and will not be included within the market schedule where COD is not Accepted.
Notes: <number>

## Slide 30
WD1 – Technical Offer Data
Trading Day D
Ending Overlap
Optimisation Period
WD1 Gate Window
GWO
11:30 TD-1
GWC
08:00 TD
TOD for entire Optimisation Time Horizon
WD1 Trading Window
Starting Overlap
Optimisation Period
Technical Offer Data
Forecast Avail, MSG, MINOUT
If no Accepted EA1 Forecasts, Starting Gate Window Data = Default Data.
For VTOD use latest Accepted Data = EA2 Set Selection if Accepted, otherwise EA1 Set Selection if Accepted, otherwise Default Data.
Other Technical Offer Data = Default Data
Notes: <number>

## Slide 31
WD1 Contingency Data (HLD section 3.5.4)
Data Transaction | WD1 Contingency Data
Four Day Load Forecast | Most recent Four Day Load Forecast Accepted by the relevant Gate Window Closure
Wind Power Unit Forecast | Most recent Wind Forecast Accepted by the relevant Gate Window Closure
Interconnector Available Transfer Capacity | Most recent ATC data Accepted by the relevant Gate Window Closure
Modified Interconnector Unit Nominations | MIUNs if available from the EA2 MSP Software Run. If not, IUNs if available from the EA2 MSP Software Run. MIUNs if available from the EA1 MSP Software Run. If not, IUNs if available from the EA1 MSP Software Run. Otherwise, zeros will be used.
Load Forecast is submitted each day for at least the following four Calendar Days.
Wind Forecast is submitted once prior to the EA1 Gate Window Closure and as updated
ATC is submitted each day for the following Trading Day and associated Ending Overlap Optimisation Period.
Various contingencies agreed as part of the High Level Design, to ensure that the best information is used for Interconnector Units in relation to previously traded quantities.
The MSP Software pre-processor will identify when sufficient data is not available and Contingency Data needs to be used.
The Contingency Data is always based on the latest Accepted data.
Notes: <number>

## Slide 32
No change from the current calculation.
Will utilise Accepted COD/TOD by the WD1 Gate Window Closure.
For External Data Providers (e.g. TSOs), latest data received will be used.
WD1 – Calculation of Schedule Demand
Demand Forecast
(A)
Nominated
Quantity
(B)
Forecast
Availability
Wind
Forecast
MINUS
MIN(A,B)
Affected Units
Demand Forecast, net of Autonomous Non-Wind
PPTG Non-Wind,
VPTG Non-Wind,
PPMG Under Test Non-Wind,
VPMG Under Test Non-Wind
(A)
Wind
Forecast
(B)
Forecast
Availability
MIN(A,B)
VPTG Wind,
VPMG Under Test Wind
MINUS
MINUS
Data Source
Autonomous Wind
System Operators
Participants via COD/TOD submitted by WD1 Gate Window Closure
Forecast Availability via TOD submitted by WD1 Gate Window Closure
Wind Forecast from System Operators
System Operators
Calculation
Notes: <number>

## Slide 33
For the WD1 MSP Software Run, Capacity Holdings are not required.
Any Interconnector User may trade via an Interconnector on which they have registered.
For Interconnectors as a whole, MSQs will be limited in aggregate by the Interconnector Ramp Rate and Interconnector Import and Export ATC, treating both the EA1 and EA2 MIUNs as fixed:
WD1 – Interconnector Constraints
The maximum export capacity for the Interconnector
MSQ for the Interconnector Unit that is optimised by the WD1 MSP Software Run
Latest MIUNs for the Units optimised by the EA1 MSP Software Run treated as fixed
The maximum import capacity for the Interconnector
Latest MIUNs for the Units optimised by the EA2 MSP Software Run treated as fixed
Notes: <number>

## Slide 34
For Interconnector Units, Active Capacity Holdings are not required.
Instead, WD1 MSQs are only limited in accordance with the maximum import/export trades as submitted by the Participant in their Commercial Offer Data to the WD1 Gate Window.
WD1 – Interconnector Unit Constraints
Price
Quantity
Lower
Operating
Limit *
Higher
Operating
Limit
Range within which the MSQ may be
optimised by the MSP Software
Where:
MIUEC Maximum Interconnector Unit Export Capacity
MIUIC Maximum Interconnector Unit Import Capacity
* May be set to zero where PQ Pairs have been excluded as part of the calculation of Offered Modified PQ Pairs (Appendix P)
Notes: <number>

## Slide 35
WD1 Gate Window Closure 08:00
Notes: Key points:
All can bid to each Gate (other than non Capacity Holders in EA1).
As per EU guidelines, EA2 is the opportunity reallocate Interconnector capacity on D-1 and WD1 is the opportunity to reallocate on D.
<number>

## Slide 36
WD1 MSP Software Run by 09:30
Notes: Key points:
All can bid to each Gate (other than non Capacity Holders in EA1).
As per EU guidelines, EA2 is the opportunity reallocate Interconnector capacity on D-1 and WD1 is the opportunity to reallocate on D.
<number>

## Slide 37
Contents
Introduction
EA1 MSP Software Runs
EA2 MSP Software Runs
WD1 MSP Software Runs
EP1 MSP Software Runs
EP2 MSP Software Runs
MSP Software Run Cancellation
Treatment of Energy Limited Units
Other Data Transactions
Publications & Reports
Required Credit Cover Query
Glossary
Notes: <number>

## Slide 38
Highlights:
  Commercial Offer Data will be the latest Accepted (submitted and validated) and Utilised (used in a completed MSP Software Run). Hence COD may be different for Trading Periods in the first and second portion of the EP1 or EP2 Optimisation Time Horizons.
  Technical Offer Data will be the latest Accepted (submitted and validated) and Utilised (used in a completed MSP Software Run). The same TOD will apply for the entire EP1 or EP2 Optimisation Time Horizon.
  Interconnector Users will have Interconnector Units for all Gate Windows to which they submitted COD. For example, if an Interconnector User bids to all of the Gate Windows, there will be three Interconnector Units, for that Interconnector User, for which MSQs are calculated in the EP1 or EP2 runs.
EP1 & EP2 – No significant change
Notes: <number>

## Slide 39
Each MSP Software Run needs Initial Conditions at the start of the Optimisation Time Horizon:
  Initial Status (ON or OFF)
  Initial MW (MSQ from last Trading Period in the previous Trading Day).
  Last Status Change Date/Time
  First Available Time
  Start Up Cost Carried over
  Start Up Time Hot/Warm/Cold
For EP1, the Initial Conditions will be taken from the EP1 MSP Software Run for the previous Trading Day.
EP1 – Initial Conditions
Trading Day D-1
Trading Day D
Ending Overlap
Optimisation Period
Initial
Conditions
Ending Overlap
Optimisation Period
Initial Conditions from EP1 for the previous Trading Day
Notes: <number>

## Slide 40
EP1 – Commercial Offer Data
Trading Day D
Ending Overlap
Optimisation Period
Commercial Offer Data
Price Quantity Pairs
No Load Costs
Start Up Costs
Shut Down Costs
Decremental Price
Maximum Interconnector Unit Import Capacity
Maximum Interconnector Unit Export Capacity
For each Trading Period in the EP1 Trading Window:
COD for Interconnector Units = Calculated Offered Modified PQ Pairs and Accepted Max Import/Export Capacities.
For other Generator Units, latest Accepted and Utilised COD
e.g. Accepted EA2 COD for Trading Periods 06:00 to 17:30, where EA2 MSP Software Run is not cancelled.
e.g. Accepted WD1 COD for Trading Periods 18:00 to 11:30, where WD1 MSP Software Run is not cancelled.
EP1 Trading Window
Latest Accepted and Utilised COD for each Trading Period (EA2/WD1)
Notes: <number>

## Slide 41
EP1 – Technical Offer Data
Trading Day D
Ending Overlap
Optimisation Period
Technical Offer Data
VTOD Set Selection
Forecast Avail, MSG, MINOUT
Other Technical Offer Data
EP1 MSP Software Run uses the latest Accepted and Utilised Technical Offer Data for each Trading Period. This will take account of MSP Software Cancellation.
Technical Offer Data
VTOD Set Selection
Forecast Avail, MSG, MINOUT
Other Technical Offer Data
EA1 Trading Window
EA2 Trading Window
WD1 Trading Window
Technical Offer Data
Forecast Avail, MSG, MINOUT
EA1 Gate Window:
EA2 Gate Window:
WD1 Gate Window:
Notes: <number>

## Slide 42
EP1 – Calculation of Schedule Demand (06:00 to 00:00)
No change from the current calculation (to midnight on the Trading Day).
Affected Units
Price Maker Generator Units not Under Test
PPTG, PPMG Under Test
VPTG, VPMG Under Test
Data Source
System-wide
Meter Data Providers or Market Operator where MGuh defined otherwise
Participants via COD/TOD- latest Accepted values utilised per Trading Period.
Derived by MO from data submitted by TSOs.
System Operators
Meter Data Providers
Derived by MO from data submitted by TSOs.
Interconnector Residual Capacity Units (IRCU)
System Operators, for SO Interconnector Trades
DQ set by Market Operator based on this data
06:00
00:00
12:00
Calculation
Actual Output
(A) min(Nominated
Quantity, Availability
Profile or Actual
Availability)
(B)
Actual
Output
Demand
Control
MINUS
A-B
(A)
Availability
Profile
(B)
Actual Output
A-B
MINUS
PLUS
DQ for
IRCU
PLUS
Notes: <number>

## Slide 43
EP1 – Calculation of Schedule Demand (00:00 to 12:00)
No change from the current calculation (from midnight on the Trading Day).
06:00
00:00
12:00
Demand Forecast
(A)
Nominated
Quantity
(B)
Forecast
Availability
Wind
Forecast
MINUS
MIN(A,B)
Affected Units
Demand Forecast, net of Autonomous Non-Wind
PPTG Non-Wind,
VPTG Non-Wind,
PPMG Under Test Non-Wind,
VPMG Under Test Non-Wind
(A)
Wind
Forecast
(B)
Forecast
Availability
MIN(A,B)
VPTG Wind,
VPMG Under Test Wind
MINUS
MINUS
Data Source
Autonomous Wind
System Operators
Participants via COD/TOD submitted by WD1 Gate Window Closure
Forecast Availability via TOD submitted by WD1 Gate Window Closure
Wind Forecast from System Operators
System Operators
Calculation
Notes: <number>

## Slide 44
As for the current Ex-Post MSP Software Run, there will be no constraints in the MSP Software for EP1 which relate to an Interconnector as a whole.
Instead, the same constraints will apply for Interconnector Units as are currently applied with the Ex-Ante Market Schedule.
MSQs will be limited by the MIUNs allocated in EA1, EA2 and WD1 Runs (or as adjusted if ATC changes within day)
EP1 – Interconnector/Interconnector Unit Constraints
Price
Quantity
Lower
Operating
Limit
Higher
Operating
Limit
Range within which the MSQ (=IUN) may be optimised by the MSP Software
Note: MIUNs will not exceed the corresponding IUNs for each Interconnector Unit.
Notes: <number>

## Slide 45
Contents
Introduction
EA1 MSP Software Runs
EA2 MSP Software Runs
WD1 MSP Software Runs
EP1 MSP Software Runs
EP2 MSP Software Runs
MSP Software Run Cancellation
Treatment of Energy Limited Units
Other Data Transactions
Publications & Reports
Required Credit Cover Query
Glossary
Notes: <number>

## Slide 46
Each MSP Software Run needs Initial Conditions at the start of the Optimisation Time Horizon:
  Initial Status (ON or OFF)
  Initial MW (MSQ from last Trading Period in the previous Trading Day).
  Last Status Change Date/Time
  First Available Time
  Start Up Cost Carried over
  Start Up Time Hot/Warm/Cold
For EP2, the Initial Conditions will be taken from the EP2 MSP Software Run for the previous Trading Day.
EP2 – Initial Conditions
Trading Day D-1
Trading Day D
Ending Overlap
Optimisation Period
Initial
Conditions
Ending Overlap
Optimisation Period
Initial Conditions from EP2 for the previous Trading Day
Notes: <number>

## Slide 47
EP2 – Commercial Offer Data
Trading Day D
Ending Overlap
Optimisation Period
Commercial Offer Data
Price Quantity Pairs
No Load Costs
Start Up Costs
Shut Down Costs
Decremental Price
Maximum Interconnector Unit Import Capacity
Maximum Interconnector Unit Export Capacity
For each Trading Period in the EP2 Trading Window:
COD for Interconnector Units = Calculated Offered Modified PQ Pairs and Accepted Max Import/Export Capacities.
For other Generator Units, latest Accepted and Utilised COD
e.g. Accepted EA2 COD for Trading Periods 06:00 to 17:30, where EA2 MSP Software Run is not cancelled.
e.g. Accepted WD1 COD for Trading Periods 18:00 to 11:30, where WD1 MSP Software Run is not cancelled.
EP2 Trading Window
Latest Accepted and Utilised COD for each Trading Period (EA2/WD1)
Notes: <number>

## Slide 48
EP2 – Technical Offer Data
Trading Day D
Ending Overlap
Optimisation Period
Technical Offer Data
VTOD Set Selection
Forecast Avail, MSG, MINOUT
Other Technical Offer Data
EP2 MSP Software Run uses the latest Accepted and Utilised Technical Offer Data for each Trading Period. This will take account of MSP Software Cancellation.
Technical Offer Data
VTOD Set Selection
Forecast Avail, MSG, MINOUT
Other Technical Offer Data
EA1 Trading Window
EA2 Trading Window
WD1 Trading Window
Technical Offer Data
Forecast Avail, MSG, MINOUT
EA1 Gate Window:
EA2 Gate Window:
WD1 Gate Window:
Notes: <number>

## Slide 49
No change to EP2 calculation of Schedule Demand.
EP2 – Calculation of Schedule Demand
Actual Output
(A) min(Nominated
Quantity, Availability
Profile or Actual
Availability)
(B)
Actual
Output
Demand
Control
MINUS
A-B
Affected Units
Price Maker Generator Units not Under Test
PPTG, PPMG Under Test
(A)
Availability
Profile
(B)
Actual Output
A-B
VPTG, VPMG Under Test
MINUS
PLUS
Data Source
System-wide
Meter Data Providers or Market Operator where MGuh defined otherwise
Participants via COD/TOD- latest Accepted values utilised per Trading Period.
Derived by MO from data submitted by TSOs.
System Operators
Meter Data Providers
Derived by MO from data submitted by TSOs.
DQ for
IRCU
Interconnector Residual Capacity Units (IRCU)
System Operators, for SO Interconnector Trades
DQ set by Market Operator based on this data
Calculation
PLUS
Notes: <number>

## Slide 50
As for the current Ex-Post MSP Software Run, there will be no constraints in the MSP Software for EP2 which relate to an Interconnector as a whole.
Instead, the same constraints will apply for Interconnector Units as are currently applied with the Ex-Ante Market Schedule.
MSQs will be limited by the MIUNs allocated in EA1, EA2 and WD1 Runs (or as adjusted if ATC changes within day)
EP2 – Interconnector/Interconnector Unit Constraints
Price
Quantity
Lower
Operating
Limit
Higher
Operating
Limit
Range within which the MSQ (=IUN) may be optimised by the MSP Software
Note: MIUNs will not exceed the corresponding IUNs for each Interconnector Unit.
Notes: <number>

## Slide 51
Contents
Introduction
EA1 MSP Software Runs
EA2 MSP Software Runs
WD1 MSP Software Runs
EP1 MSP Software Runs
EP2 MSP Software Runs
MSP Software Run Cancellation
Treatment of Energy Limited Units
Other Data Transactions
Publications & Reports
Required Credit Cover Query
Glossary
Notes: <number>

## Slide 52
MSP Software Run Cancellation
The Intra-Day Trading High Level Design allows for cancellation of some MSP Software Runs, in the event that the relevant MSP Software Run is delayed beyond 30 minutes after the relevant Gate Window Closure.
The cancellation of runs will not apply to any EA1 MSP Software Run or Ex-Post MSP Software Run.
Cancellation will be initiated by a Market Operator user, via the Market Operator Interface.
Notes: <number>

## Slide 53
MSP Software Run - Cancellation Provisions
EA1 MSP Software Runs cannot be cancelled under any circumstances
  Instead, EA1 delays may result in the cancellation of subsequent ex-ante runs (EA2, WD1) for the relevant Trading Day.
EP1 MSP Software Runs cannot be cancelled under any circumstances
EP2 MSP Software Runs cannot be cancelled under any circumstances
As a result, only EA2 and WD1 MSP Software Runs can be cancelled
Notes: <number>

## Slide 54
MSP Software Run – EA2 Cancellation Provisions
EA2 MSP Software Runs shall be cancelled by the Market Operator if any of the following conditions are met:
# | Cancellation Trigger | Notes
1 | EA1 MSQs and SMPs have not been published by 11:00 TD-1 (EA1 publication deadline). | Cancellation avoids EA2 publishing time delays and Interconnector User MIUNs provision delays.
2 | ATC data for all Interconnectors in the SEM have not been Accepted by the scheduled EA2 Gate Window Closure time (i.e. not received at all for Trading Day). | No limits on the EA2 IUNs (the MSP Software needs this data for EA2/WD1).
3 | EA2 Gate Window is not closed by 30 minutes after the scheduled EA2 Gate Window Closure time. | Cancellation avoids EA2 publishing time delays and Interconnector User MIUNs provision delays. If not cancelled, Operations Schedule (RCUC) would be delayed.
4 | Ex-Ante Two MSP Software Run cannot be run as at 30 minutes after the EA2 Gate Window Closure. | Alternative would be Administered Schedule/Prices – no advantage to this.
5 | At the time that is 30 minutes after the EA2 Gate Window Closure, the Central Market System is experiencing technical difficulties such that its reporting function is disabled. | If cannot publish, Interconnector Users will not have a known position against which to trade in BETTA and there would be an Operations Schedule (RCUC) delay. Alternative would be Administered Schedule/Prices – no advantage to this (unrealistic RCUC schedule, no Interconnector trades)
Notes: <number>

## Slide 55
MSP Software Run – WD1 Cancellation Provisions
WD1 MSP Software Runs shall be cancelled by the Market Operator if any of the following conditions are met:
# | Cancellation Trigger | Note
1 | EA1 MSP Software Run for the same Trading Day has not been completed by the WD1 Gate Window Closure | Unlikely to happen – Administered Schedule and Prices would occur first.
2 | EA2 MSQs and SMPs have not been published by 30 minutes before the WD1 Gate Window Closure. | If cannot publish, Interconnector Users will not have a position to trade in BETTA and will not know what remaining capacity is available.
3 | ATC data for all Interconnectors in the SEM have not been Accepted by the scheduled WD1 Gate Window Closure time (i.e. not received at all for Trading Day). | No limits on the EA2 IUNs (the MSP Software needs this data for EA2/WD1).
4 | WD1 Gate Window is not closed by 30 minutes after the scheduled WD1 Gate Window Closure time. | Cancellation avoids WD1 publishing time delays and Interconnector User MIUNs provision delays.
5 | Within Day One MSP Software Run cannot be run as at 30 minutes after the WD1 Gate Window Closure. | Alternative would be Administered Schedule/Prices – no advantage to this.
6 | At the time that is 30 minutes after the WD1 Gate Window Closure, the Central Market System is experiencing technical difficulties such that its reporting function is disabled. | If cannot publish, Interconnector Users will not have a known position against which to trade in BETTA. Alternative would be Operations Schedule (RCUC) delay.
Notes: <number>

## Slide 56
When MSP Software Run Cancellation occurs:
  An MSP Software Run Cancellation Report will immediately be produced, containing:
    Run Type
    Affected Trading Day
    Date and Time of Cancellation
  MSP Software Run Cancellation reports will be produced in XML and HTML formats and will be accessible via the MPI and can therefore be:
    Downloaded via Type 3 (Webservice request)
    Viewed via Type 2 (MPI)
  Notification of the production of an MSP Software Run Cancellation report will be accessible via the Market Message Window, as part of the MPI.
MSP Software Run Cancellation Report
Notes: <number>

## Slide 57
Contents
Introduction
EA1 MSP Software Runs
EA2 MSP Software Runs
WD1 MSP Software Runs
EP1 MSP Software Runs
EP2 MSP Software Runs
MSP Software Run Cancellation
Treatment of Energy Limited Units
Other Data Transactions
Publications & Reports
Required Credit Cover Query
Glossary
Notes: <number>

## Slide 58
Technical Offer Data for Energy Limited Units includes the following data:
  Energy Limit
    In MWh for the Trading Day, limiting the MSQ for the Energy Limited Unit in the Trading Day.
  Energy Limit Factor
    Must be 0.25, multiplied by the Energy Limit to give the energy limit for the Ending Overlap Optimisation Period
  Energy Limit Start
    Must be the first Trading Period in the Trading Day
  Energy Limit Stop
    Must be the last Trading Period in the Trading Day
There will be no change from the current implementation for Intra-Day Trading (MSP Software will not exceed the Energy Limit for the relevant period).
Treatment of Energy Limited Units
Trading Day D
Ending Overlap
Optimisation Period
Energy Limit Period (Energy Limit Start to Energy Limit Stop)
Energy limit for EOOP = Energy Limit * Energy Limit Factor
Notes: <number>

## Slide 59
Contents
Introduction
EA1 MSP Software Runs
EA2 MSP Software Runs
WD1 MSP Software Runs
EP1 MSP Software Runs
EP2 MSP Software Runs
MSP Software Run Cancellation
Treatment of Energy Limited Units
Other Data Transactions
Publications & Reports
Required Credit Cover Query
Glossary
Notes: <number>

## Slide 60
Data Transactions (TSO-MO) for Intra-Day Trading
SEMO
(MI)
Annually
TSO
TSO
TSO
TSO
Following MSP Software Run
INBOUND
Following MIUN Calculation
TSO
TSO
01) System Parameters
02) Loss Adjustment Factors
03) Ex-Post Loss of Load Probability Table
04) Annual Load Forecast
05) Uninstructed Imbalance Parameters
06) Testing Tariffs
TSO
TSO
TSO
Monthly
TSO
INBOUND
TSO
07) Loss of Load Probability for the Capacity Period
08) Monthly Load Forecast
Daily
TSO
TSO
INBOUND
TSO
09) Generator Unit Technical Characteristics
10) Demand Control
11) System Characteristics
12) Energy Limited Unit Technical Characteristics
13) Dispatch Instructions
14) SO Interconnector Trades
15) Four Day Load Forecast
16) Wind Power Unit Forecast
17) Forecast Ex-Post Loss of Load Probability
TSO
TSO
TSO
TSO
TSO
TSO
OUTBOUND
24) Ex-Ante One Market Schedule
25) Ex-Ante Two Market Schedule
26) Within Day One Market Schedule
27) Ex-Post Indicative Market Schedule
28) Ex-Post Initial Market Schedule
Ad Hoc
TSO
33) Commencement Notice
34) Deregistration Notice
35) Available Transfer Capacity
Following each Gate Window Closure
19) Interconnector Unit Bids and Offers
20) Other Generator Bids and Offers
21) Unit Operational Characteristics
22) Interconnector Registration (EA1 only)
23) Interconnector Characteristics (EA1 only)
29) Aggregate Modified Interconnector Unit Nominations
TSO
TSO
OUTBOUND
OUTBOUND
OUTBOUND
TSO
TSO
TSO
Following Trading Day
TSO
31) Jurisdiction Error Supplier Unit Volumes
32) Net Demand Adjustment
TSO
OUTBOUND
TSO
TSO
TSO
TSO
TSO
Notes: <number>

## Slide 61
Summary of changes for Data Transactions (TSO-MO) for Intra-Day Trading
Data Transaction | Content of File | Timing of Submission
INBOUND: Four Day Load Forecast | Data for each Trading Period in at least four complete Calendar Days for the relevant Jurisdiction. | To be submitted at least once prior to the EA1 Gate Window Closure and will be submitted as updated.
INBOUND: Wind Power Unit Forecast | Data for each Trading Period in the next two complete Trading Days (EA1/EA2) or the current and following Trading Day (WD1) for the relevant Jurisdiction. | To be submitted at least once prior to the EA1 Gate Window Closure and will be submitted as updated.
OUTBOUND: Market Schedules | For all Generator Units included within the MSP Software, for each Trading Period in the Optimisation Time Horizon. | Provided following each MSP Software Run.
OUTBOUND: Bids and Offers, Unit Operational Characteristics | Commercial and Technical Offer Data that is: Accepted for non Interconnector Units, or Offered Modified for Interconnector Units. | Provided following each Gate Window Closure.
OUTBOUND: Interconnector Registration Data, Characteristics | Interconnector Registration Data, plus Active Interconnector Unit Capacity Holdings | Provided following the EA1 Gate Window Closure.
OUTBOUND: Available Transfer Capacity | ATC for the relevant Interconnector for the Optimisation Time Horizon | Provided immediately following receipt from Interconnector Administrator.
Notes: <number>

## Slide 62
Data Transactions (IA-MO) for Intra-Day Trading
SEMO
(MI)
Ad Hoc
IA
Following MSP Software Run
IA
Following MIUN Calculation
IA
IA
IA
Daily
INBOUND
01) Available Transfer Capacity
02) Active Capacity Holdings
03) Ex-Post Interconnector Trades
04) Available Transfer Capacity
05) Interconnector Registration Data
INBOUND
IA
OUTBOUND
IA
IA
06) Interconnector Unit Nominations
OUTBOUND
07) Modified Interconnector Unit Nominations
08) Interconnector Dispatch Schedule
Notes: <number>

## Slide 63
Summary of changes for Data Transactions
(IA-MO) for Intra-Day Trading
Data Transaction | Content of File | Timing of Submission
INBOUND (Daily): Available Transfer Capacity | Data for each Trading Period in the relevant Optimisation Time Horizon. | To be submitted by 10:00 on TD-2 and as updated.
INBOUND: Active Interconnector Capacity Holdings | Data for each Capacity Holder for the relevant Optimisation Time Horizon. | To be submitted by the EA1 Gate Window Closure.
INBOUND: Ex-Post SO Interconnector Trades | No change | No change
INBOUND (Ad Hoc): Available Transfer Capacity | Maximum Import/Export Available Transfer Capacity Values and associated times for the relevant Optimisation Time Horizon. | Submitted as available, when ATC changes.
INBOUND: Interconnector Registration Data | No change | No change
OUTBOUND: Interconnector Unit Nominations | For all Interconnector Units included within the MSP Software Run, for each Trading Period in the Optimisation Time Horizon. | Provided following each MSP Software Run.
OUTBOUND: Modified Interconnector Unit Nominations | For all Interconnector Units included within the most recent MSP Software Run, for each Trading Period in the Optimisation Time Horizon. | Provided following each calculation of MIUNs.
OUTBOUND: Interconnector Dispatch Schedule | Dispatch schedule for the relevant Interconnector in the Optimisation Time Horizon. | Provided following each calculation of MIUNs.
Notes: <number>

## Slide 64
Contents
Introduction
EA1 MSP Software Runs
EA2 MSP Software Runs
WD1 MSP Software Runs
EP1 MSP Software Runs
EP2 MSP Software Runs
MSP Software Run Cancellation
Treatment of Energy Limited Units
Other Data Transactions
Publications & Reports
Required Credit Cover Query
Glossary
Notes: <number>

## Slide 65
Publication and reporting under Intra-Day Trading
For the SEM, publication and reporting are interpreted as follows:
  Publication – publicly available (General Public).
  Reporting – available to one or all Participants (Member Private or Member Public).
SEMO has drafted the provisions for publication and reporting such that ex-ante and within day data will be published as soon as possible.
  For example, the publication time for each ex-ante market schedule will be 90 minutes after the associated Gate Window Closure (rather than one day after the Trading Day as currently).
No change to any publication timings for:
  Periodic, Annual or Monthly publications/reports.
  Ex-Post publications/reports.
Notes: <number>

## Slide 66
Summary of IDT publications (Ex-Ante/Within Day)
WD1 GWC
EA1 GWC
EA2 GWC
TRADING DAY
TRADING DAY-1
TRADING DAY-2
Available Transfer Capacity (10:30)
Trading Day Exchange Rate (17:00)
Four Day Load Forecast (09:30)
Two Day Rolling Wind Power Unit Forecast, aggregated by Jurisdiction (09:30)
Active Interconnector Unit Export/Import Capacity Holding (09:30)
Ex-Ante One Market Schedule (11:00)
MIUNs (11:00)
SMP / Shadow Prices (11:00)
COD / TOD (11:00)
Ex-Ante Two Market Schedule (13:00)
MIUNs (13:00)
SMP / Shadow Prices (13:00)
COD / TOD (13:00)
Forecast Ex-Post LOLP (16:30)
Within Day One Market Schedule (09:30)
MIUNs (09:30)
SMP / Shadow Prices (09:30)
COD / TOD (09:30)
Ad Hoc Publications:
MSP Software Run Cancellation Report
MIUNs, where recalculated
Four Day Load Forecast, where updated
Wind Power Unit Forecast, where updated
Available Transfer Capacity, where updated
Notes: <number>

## Slide 67
Summary of IDT MPI-only reports (Ex-Ante/Within Day)
WD1 GWC
EA1 GWC
EA2 GWC
TRADING DAY
TRADING DAY-1
TRADING DAY-2
Daily Load Forecast Summary (09:30)
Ex-Ante One Market Schedule Detail / IUNs (11:00)
Available Credit Cover (11:00)
Excluded Bids (after EA2 GWC)
Ad Hoc Publications:
List of Active Units
List of Active Market Participants
List of Active Market Participants and Units
List of Suspended/Terminated Participants
Excluded Bids (after EA1 GWC)
Ex-Ante Two Market Schedule Detail / IUNs(13:00)
Available Credit Cover (13:00)
Required Credit Cover (14:30)
Ex-Ante Indicative Actual Schedule (16:00)
Excluded Bids (after WD1 GWC)
Within Day One Market Schedule Detail / IUNs (09:30)
Available Credit Cover (09:30)
Notes: <number>

## Slide 68
Contents
Introduction
EA1 MSP Software Runs
EA2 MSP Software Runs
WD1 MSP Software Runs
EP1 MSP Software Runs
EP2 MSP Software Runs
MSP Software Run Cancellation
Treatment of Energy Limited Units
Other Data Transactions
Publications & Reports
Required Credit Cover Query
Glossary
Notes: <number>

## Slide 69
A new query process is proposed, allowing Participants to query the calculation of Required Credit Cover, as performed by the Market Operator and provided to Participants each Working Day.
SEMO believes that this additional formal query is required, as Required Credit Cover is used as an input to the Available Credit Cover sufficiency checks for Participants with Interconnector Units.
The Required Credit Cover Query is similar to that for a Data Query or Settlement Query, with a dedicated form and timelines.
Where resolution is not identified within the maximum timescales (5WD or up to 10WD by agreement), the Market Operator will deem the issue as a Dispute.
If a Participant is not satisfied with the resolution of a Required Credit Cover Query, a Dispute may be raised.
Required Credit Cover Query
Notes: <number>

## Slide 70
Required Credit Cover Query
Raise
Required Credit
Cover (RCC)
Query
Log RCC
Query (reject if
not complete)
Investigate
and identify
resolution
Notify whether
query is upheld
Resolve Query
Notify Raising Party
of resolution
Start
Stop
Request more
time to resolve
Raise / deem as
Dispute
Notes: <number>

## Slide 71
Since WG9, SEMO has been investigating the possibility of including an Excluded Bids Query in the Code.
SEMO is conscious that Participants may wish to query the calculation of Excluded Bids (i.e. the application of Appendix P of the Code). However, the calculation of Excluded Bids is an automated process which is based mainly on the RCC.
A formal Excluded Bids Query process would:
  require retrospective change to MIUN positions (which is neither practical or desirable).
  be limited mainly to system defects (which would take time to resolve in any case).
  only be valuable if it could be resolved and affected data amended by the next Gate Window Closure (which is impractical).
  require significant additional SEMO resources that would need to be available to address queries immediately following Gate Window Closure.
SEMO proposes that queries pertaining to excluded bids be raised via the Market Helpdesk as a general query with urgent status.
Query for Excluded Bids calculations
Notes: <number>

## Slide 72
Contents
Introduction
EA1 MSP Software Runs
EA2 MSP Software Runs
WD1 MSP Software Runs
EP1 MSP Software Runs
EP2 MSP Software Runs
MSP Software Run Cancellation
Treatment of Energy Limited Units
Other Data Transactions
Publications & Reports
Required Credit Cover Query
Glossary
Notes: <number>

## Slide 73
Glossary (1)
 | Acronym | Description
Actual Output | AO | means the Active Power produced by a Generator Unit at the Export Point.
Contingency Data |  | means, in respect of certain Data Transactions, the data that is used when a Data Transaction is not Accepted by the Market Operator in accordance with the required submission timescales.
Daylight Saving Conditions |  | means the practice of temporarily adjusting clocks to be one hour ahead of local standard time during the summer, in order to provide extra daylight in the evenings during such period.
Interconnector Dispatch Schedule |  | means the set of Output values and associated times for an Interconnector, calculated by the Market Operator in the Modified Interconnector Unit Nominations calculation, in accordance with Agreed Procedure 2 “Interconnector Unit Capacity Right Calculation and Dispatch Notifications”.
Market Operator Performance Report |  | means a report prepared by the Market Operator and provided to the Regulatory Authorities, in accordance with paragraph 2.144.
MIUN Calculation Batch Identifier |  | means a unique identifier of a single set of data used as an input to the MIUN Calculator as part of a calculation of Modified Interconnector Unit Nominations for a Trading Day.
MIUN Calculator |  | means the software used by the Market Operator to determine the Modified Interconnector Unit Nominations, Interconnector Dispatch Schedule, Interconnector Unit Dispatch Schedule and Profiled SO Interconnector Trades.
Notes: <number>

## Slide 74
Glossary (2)
 | Acronym | Description
MSP Software Run |  | means the operation of the MSP Software used by the Market Operator to determine Market Schedule Quantities for each Price Maker Generator Unit and to determine the System Marginal Price for each Trading Period as defined in Appendix N.
MSP Software Run Cancellation |  | means, in respect of a particular MSP Software Run Type for a specific Trading Day, the determination by the Market Operator that the conditions which require that the MSP Software Run Type shall not be performed are met.
MSP Software Run Type |  | means one of the following types of run of the MSP Software: Ex-Ante One MSP Software Run, Ex-Ante Two MSP Software Run, Within Day One MSP Software Run, Ex-Post Indicative MSP Software Run or Ex-Post Initial MSP Software Run which are defined within Appendix N: “Operation of the MSP Software”.
Required Credit Cover Query |  | means a query by a Participant in respect of the inputs to, or calculation of, its Required Credit Cover in accordance with paragraphs 6.234A to 6.234C.
Utilised |  | means, in respect of a particular MSP Software Run Type for a Trading Day, the data that was used by the Market Operator to produce the associated Market Schedule Quantities, where the particular MSP Software Run was successfully completed and no MSP Software Run Cancellation was applied.
Notes: <number>