## Slide 1
Mod_18_10 Intra Day Trading
Working Group 5
  SOs Impact Assessment
  5th October 2010

## Slide 2
Contents:
Overview of RCUC
RCUC Changes - Impact Assessment
Market Schedule Vs Operational Schedule
Update on Other Issues
Notes: <number>

## Slide 3: Overview of RCUC
Reserve Constrained Unit Commitment (RCUC)
  Software tool used by the SOs to perform Unit Commitment and Economic Dispatch.
RCUC input data:
  Generator/IC data: COD, TOD, MIUNs
  SO data: load and wind forecasts, constraints, real time availability/output.
RCUC Outputs:
  Scheduled output for each unit for each trading period that is technically feasible.
Notes: <number>

## Slide 4: Overview of RCUC
Differences Between RCUC and UUC (the Market Schedule):
Ex- Ante UUC calculates MSQ (Market Scheduled Quantity) for each unit and takes account of the following
  COD (Price Quantity Pairs, No Load Costs and Start-Up costs)
  TOD
  Forecast system demand and wind output
  Energy limits for energy limited plant such as Hydro & Pumped Storage
RCUC takes account of each of the above and the following when calculating the DSQ for each unit
  Reserve Requirements & Reserve Capability Curves
  Transmission Constraints
  Forbidden Zones
Furthermore RCUC accurately models
  Generator Loading up and down rates from zero to Min Load (ignored in UUC)
  Actual Ramp Rates (averaged in UUC)
Notes: <number>

## Slide 5: Overview of RCUC Dispatch Scheduling
At every Trading Period, the Operational Schedule should:
  meet forecast demand
  meet required reserve
  be technically feasible
  guideline for the real time dispatch process
The Operational Schedule should also:
  minimise total production cost on the island
  be produced and communicated in a timely fashion
  be flexible enough to allow for deviations from forecasted demand, wind generation and availabilities
  provide info to Generators who have daily fuel purchasing commitments

## Slide 6: Overview of RCUC Scheduling Process
A single schedule is jointly produced by EirGrid and SONI for the Island
Operational Scheduling currently occurs in two separate time frames
  Day-ahead
  In-day
Day-Ahead Schedules
  Jointly produced by the Control Office in EirGrid and SONI
  Cover the time period from 06:00 on D up to 11:30 on D + 1
  Completed and published by 16:00 on D-1
  Updated as required and republished at 01:00

## Slide 7: Overview of RCUC Scheduling Process cont’d
In-Day Schedules
  Jointly produced in real time by Control Centres in EirGrid and SONI
  Day Ahead is updated with latest information and becomes the In-Day schedule at 06:00
  End time of the In-Day schedule is always 11:30 D+1, starting time varies
  Revised In-Day schedules published at 06:00, 11:00 and 20:00 (times are approximate – NCC dependent)

## Slide 8: RCUC Changes - Impact Assessment
SOs have been discussing possible RCUC changes to facilitate intra day trading with ABB.
Initial assessment from ABB is that these changes are achievable.
SOs have assumed that there is no change to Technical Offer Data (TOD) within day.
Notes: <number>

## Slide 9
Market Schedule Vs Operational Schedule
There will always be differences between the Market Schedule and the Operational Schedule, e.g. Transmission constraints and Reserve constraints, changes to demand and wind forecasts, changes to generator availability, Market modelling assumptions.
Additional gate closures offer the opportunity for more up to date conditions to be reflected in the Market Schedule and should help reduce differences between the Market Schedule and Operational Schedule thus tending to reduce constraint costs, however…...
Divergence of the Market Schedule and Operational Schedule could increase if additional generator physical characteristics (which begin to bind as the time between gate closure and the start of the trading period shortens) are not taken into account in the production of the Market Schedule.
If these additional generator characteristics are not taken into account there could be also be an increase in constraint costs and the use of mitigation measures by the SOs.
Notes: <number>

## Slide 10
Market Schedule Vs Operational Schedule
The time required to synchronise a generator and get it up to minimum load can be up to 20 hours.
The market software does not take into account this time and will transition a unit from zero to minimum load in one trading period.
As current gate closure and production of the Market Schedule is approximately 18 hours before the start of the trading day, unit commitment decisions can currently be managed by the SOs to minimise any security issues although constraint costs do arise.
Notes: <number>

## Slide 14
Market Schedule Vs Operational Schedule
The SOs propose that the following options for change to the market scheduling software are assessed:
Consider the time required for an off-line generator to synchronise (this should also account for the time from gate closure to issue of the Market Schedule).
As 1 plus model a proxy of generator loading characteristics from synchronisation up to minimum generation.
As 1 plus model actual generator loading characteristics up to minimum generation.
As well as assessing the impact of these changes, any decision to implement any of these options would also be dependant on:
Modelling of the impact on market / constraint costs
SEM Committee position on the alignment of Market Schedule and Dispatch.
Notes: <number>

## Slide 15
Update on Other Issues
SO-SO Trades: Discussions under way between EirGrid and National Grid to put in place SO-SO trading arrangements for EWIC (arrangements already in place for Moyle).
Operational Schedule Production Process – The SOs are reviewing the process for production of the Operational Schedule to meet the requirements of intra day trading.
Constraining Interconnector Flows for security: participants are invited to comment on how this might be achieved from a trader perspective.
There is a significant amount of further analysis required on issues such as market/constraint modelling and generator flexibility incentives (e.g. warming contracts).
Assessment of resourcing implications will follow once decisions on gate closure times / operational schedules are known.
Notes: <number>

## Slide 16: Summary
Changes to RCUC will be required to accommodate intra day trading – initial assessment from ABB is that these modifications look feasible.
It has been assumed that there will be no TOD changes at the within day gate.
The SOs believe that consideration should be given to reflecting additional generator characteristics in the production of the Market Schedule.