## Slide 1: Demand Side Units in SEM
<number>
Notes: *
*
<number>##

## Slide 2: Trading Sites
<number>
A “Trading Site” is a device for correctly netting Energy and Capacity Payments when there is both generation and load at the same site.
With generation & load at the same site then the final settlement position will be:
  Energy payments are based on the NET generation.
  Capacity payments are based on the NET generation.
  Constraint payments and uninstructed imbalances are based on the GROSS generation while Imperfection Charge are on GROSS LOAD.
  Variable Operators Charge on GROSS load.
The Generator Units are registered by the Market Participant at that Trading Site.
There can be only one Supplier Unit at a Trading Site
Generator Units
Netting Generator Unit
Supplier Unit
T R A D I N G S I T E
Notes: *
*
<number>##

## Slide 3: Trading Sites Example
<number>
The example on the next slide assumes this is registered to the registered participant for the Trading Site (i.e. A Trading Site Supplier Unit)
Alternatively, it could be registered to another Participant (an Associated Supplier Unit) in which case the Netting Generator Unit has a zero quantity for the Trading Site participant.
The Netting Generator Unit is a virtual unit, registered by the SMO on behalf of the Market Participant at that Trading Site.
Notes: *
*
<number>##

## Slide 4: Trading Sites
<number>
Meter Data and MSQ for the Netting Generator Unit is negative of the lesser of:
  The absolute value of the total metered values for the Generator Units.
  The absolute value of the total metered values for the Supplier Units.
Energy and Capacity Payments are based on Generator Unit MSQs and the Netting Generator (which is a negative number)
Energy and Capacity Charges are based on Supplier Unit MSQs less Netting Generator Unit output (which is a negative number)
Other settlement terms are still settled on a gross basis
Generator Units
Netting Generator Unit
Supplier Unit
T R A D I N G S I T E
Generator Unit MW (A) | +100 | +50 | +40
Supplier Unit MW (B) | -60 | -80 | -40
Netting Generator Unit MW (C = -Min(¦A¦,¦B¦)) | -60 | -50 | -40
Generator Unit Energy/Capacity Payment MW (A) | +100 | +50 | +40
Netting Generator Unit Energy/Capacity Payment MW (C) | -60 | -50 | -40
Net Energy/Capacity Payment MW (A+ C) | +40 | 0 | 0
Supplier Unit Energy/Capacity Charge MW (B – C) | 0 | -30 | 0
Notes: *
*
<number>##

## Slide 5: DSU Settlement