## Slide 1
Gill Nolan & Jeffrey Godsell, PSOP
T&SC Modification Proposal: Clarification of Outturn Availability

## Slide 2: Overview
SEMC Outturn Availability Decision
Background – what is Outturn Availability?
Trading and Settlement Code Modification Proposal
  Overview
  Proposed Text
Overview of Proposed Grid Code Modification
  How Generation Units will declare Availability
  Grid Code Modification proposal
  Proposed Text changes
Other relevant information
Next steps

## Slide 3: SEMC Outturn Availability Decision
SEMC decision paper (SEM-15-071): 29th September 2015
  Joint all island TSO Consultation in February 2013 (as requested by RAs)
  “Minded to Decision Paper” published in February 2015 (SEM-15-14).
EirGrid Group Approach:
  Drafting a paper setting out the intended implementation.
  Implementation paper, with a proposed publication date, will be submitted to the RAs for their comment.
  Implementation paper will then be published on the EirGrid and SONI websites.
  Implementation for 2016 calendar year.

## Slide 4: Background
What is Outturn Availability?
  Data transaction sent by TSOs to SEM each day
  Contains availability data for each Generation Unit for the previous day.
  Determines the Generation Unit’s availability in SEM i.e. the “commercial” availability.
  At times, the technical availability of a Generation Unit and the “commercial” availability may deviate.
    E.g. Annual maintenance on connection assets or capital works associated with the relevant generation unit may disconnect a generation unit that is technically available at the connection point.
  However, this deviation should be minimal, as the TSOs schedule Annual Maintenance to coincide with Generation Unit outages whenever possible.

## Slide 5: T&SC Modification Proposal Overview
Outturn Availability is already defined in the T&SC.
Availability is already defined in the T&SC
TSC Modification Proposal: The following definitions are amended to refer to the Grid Code
  Availability
  Outturn Availability
  Primary Fuel Type Outturn Availability
  Secondary Fuel Type Outturn Availability

## Slide 6: T&SC Modification Proposal Text
Availability means a Generator Unit’s capability in MW to deliver Active Power or a Demand Side Unit’s capability of reducing the Active Power consumed on the Trading Site, declared to the TSO as required under the relevant Grid Code.
Outturn Availability means the set of Outturn Availability data (as defined under the relevant Grid Code) for a Generator Unit provided for a previous Trading Day submitted in accordance with paragraph 4.48.
Primary Fuel Type Outturn Availability means the subset of Outturn Availability data (as defined under the relevant Grid Code) for a Dual Rated Generator Unit pertaining to the Availability of the Dual Rated Generator Unit based on its Primary Fuel Type provided for a previous Trading Day submitted in accordance with paragraph 4.48.
Secondary Fuel Type Outturn Availability means the subset of Outturn Availability data (as defined under the relevant Grid Code) for a Dual Rated Generator Unit pertaining to the Availability of the Dual Rated Generator Unit based on its Secondary Fuel Type provided for a previous Trading Day submitted in accordance with paragraph 4.48.

## Slide 7: How Generation Units will declare Availability
Generation Units will declare their Availability as set out in the Grid Code i.e.
  Will declare the “technical” availability of the generation unit unless an exception applies.
The relevant generation unit will declare zero (as advised by the TSO) during:
  Up to 5 days of Annual Maintenance of transmission connection assets between the connection point and the busbar disconnects at the meshed transmission station; or
  where work to the Transmission System is being carried out that is related to the relevant Generation Unit.
This is explicitly stated in the proposed Grid Code modification

## Slide 8: Proposed Grid Code Modification Overview
The Grid Code specifies in SDC1.4.3.2 that each generator should use reasonable endeavours to ensure that it does not at any time declare the availability at levels or values different to those that the generation unit could achieve at the relevant time, with a number of exceptions, which are listed in SDC1.4.3.3.
This modification proposal adds a further exception as a new clause SDC1.4.3.3A
  Sets out that the Generation Unit shall declare an Availability of zero during the five days of Annual Maintenance or for transmission works related to the relevant Generation Unit.
A new section title and clause is added as SDC1.4.3.9, which clarifies that Outturn Availability is set equal to the declared value of Availability.
New Glossary definitions for Annual Maintenance, Outturn Availability and Outturn Availability Connection Assets.

## Slide 9: Proposed Grid Code Text (1)
SDC1.4.3.2
Each Generator, and where relevant each Generator Aggregator, shall, subject to the exceptions in SDC1.4.3.3 and SDC1.4.3.3A, use reasonable endeavours to ensure that it does not at any time declare in the case of its CDGU, Controllable WFPS, or Aggregated Generating Unit, the Availability, or Technical Parameters at levels or values different from those that the CDGU, Controllable WFPS, and/or an Aggregated Generating Unit could achieve at the relevant time. The TSO can reject declarations to the extent that they do not meet these requirements.
New Clause: SDC1.4.3.3A
“SDC1.4.3.2 shall not apply for a CDGU or Controllable WFPS during any one or more of the following:
  any Annual Maintenance outage or portion thereof on the Outturn Availability Connection Assets lasting up to and including a maximum of five days in total in a calendar year; or
  where work to the Transmission System is being carried out that is related to the relevant CDGU or Controllable WFPS. This does not include work carried out related to another Generation Unit with a different Connection Point but a shared asset.
  The relevant CDGU or Controllable WFPS shall declare Availability at a value of zero during any one or more of (a) or (b) above, as advised by the TSO.”

## Slide 10: Proposed Grid Code Text (2)
SDC1.4.3.9 Outturn Availability
Outturn Availability shall be set equal to the declared value of Availability.
Glossary
Annual Maintenance: A transmission outage for maintenance of equipment that is part of an Outturn Availability Connection Asset. A list of Annual Maintenance items will be published annually by the TSO.
Outturn Availability: The set of Availability data for the relevant CDGU, Controllable WFPS, Aggregated Generating Unit, Pumped Storage Plant Demand or Demand Side Unit as declared pursuant to SDC1.4 and submitted by the TSO to SEM after the end of the Trading Day.
Outturn Availability Connection Assets: Any transmission equipment between and including the Connection Point and the busbar disconnects at the meshed Transmission Station.

## Slide 11: Other relevant information
  February 2013 TSO consultation: “Process for the Calculation of Outturn Availability”.
    “Where a Generator installs capacity in excess of the MEC then a decision is required as to whether Outturn Availability is capped at MEC or not. We invite comments on whether Outturn Availability should be capped at MEC or not.”
  Neither the Minded to Decision Paper (Feb 2015) nor the Decision Paper (Sep 2015) specifically address this topic.
  CER Installed Capacity Cap decision in 2014 set out that Installed Capacity Cap “does not, and will not, allow generators to export at a higher level than their contracted MEC”.
  TSOs are requesting clarification from the SEMC as to whether Outturn Availability should be capped at MEC or not.

## Slide 12: Next Steps
Take feedback from the Joint Grid Code Review Panel & formally raise proposed Grid Code Modifications.
Send the Implementation Paper to the RAs for comment.
Publish Implementation Paper on EirGrid and SONI websites.