## Slide 1: Loss Adjustment When Exporting Mod 12_11 Interconnector Unit Loss Adjustment when Exporting Adjustment When Exporting Modifications Meeting on 5th April 2011
<number>
Notes: *
*
<number>##

## Slide 2: Background
<number>
Moyle Interconnector connects in Scotland and Northern Ireland
EW Interconnector will connect in the Republic of Ireland and Wales
Both are DC Interconnectors and incur losses associated with the transmission of electricity
Notes: *
*
<number>##

## Slide 3: Users of Interconnectors
<number>
The current Moyle Interconnector is used by:
  Interconnector Users, which currently need to hold capacity to trade
  System Operators, for making SO-SO Trades
Intra-Day Trading will allow any Participant to trade via the Interconnectors registered in SEM (Moyle and EWIC)
Notes: *
*
<number>##

## Slide 4: Interconnector Capacities - Moyle
<number>
Moyle currently has capacity as follows:
  Import: 410MW in summer and 450MW in winter
  Export: 295MW from Sep to Apr and 287MW from May to Aug, (increased from 80MW on 1st Feb 2011)
295
450
Notes: *
*
<number>##

## Slide 5: Interconnector Capacities - EWIC
<number>
EWIC will have capacity as follows:
  Import: 500MW
  Export: 500MW
500
500
Notes: *
*
<number>##

## Slide 6: Trading and Settlement Code terms
<number>
Each Generator Unit (including Interconnector Units) and Supplier Unit is associated with both of the following:
  Interconnector Data Submission Point: The notional point at which Interconnector Units, Interconnector Residual Capacity Units and Interconnector Error Units are deemed to be joined to the SEM and at which relevant metered values are collected, prior to Loss-Adjustment and in respect of the transmission of electricity across an Interconnector into SEM.
  Trading Boundary: A notional balancing point for generation and supply and is the point of sale for trading in the SEM.
Trading Boundary
(illustrative)
IDSP (Moyle)
IDSP (EWIC)
  Simply, the scope of the SEM is the shaded area
Notes: *
*
<number>##

## Slide 7: Loss Adjustment in the SEM
<number>
Transmission Loss Adjustment factors for Interconnectors are based on the Interconnector Data Submission Point (IDSP) in SEM jurisdictions, plus an allowance for losses on the Interconnectors to the Connection Point.
For Interconnector Units, CLAF=TLAF.
Currently, the TLAF for Moyle is approx. 0.987 (made up of losses from Ballycronan More (approx1.005) and the Moyle links (0.018)).
Trading Boundary
(illustrative)
IDSP (Moyle)
IDSP(EWIC)
Notes: *
*
<number>##

## Slide 8: Loss Adjustment in the SEM
<number>
Key payments to Interconnector Units are summarised as follows:
  Energy Payments (based on MSQLF and SMP)
    MSQ is scheduled in Ex-Post MSP Software Runs between zero and the MIUN
  Capacity Payments (based on EA)
    EA=DQ=MIUN for Interconnector Units
  Constraint Payments (based on DQLF and MSQLF)
    DQLF=MIUN*CLAF for Interconnector Units
    MSQ is scheduled in Ex-Post MSP Software Runs between zero and the MIUN and is then adjusted by CLAF for settlement
Notes: *
*
<number>##

## Slide 9: Loss Adjustment in the SEM - Importing
<number>
Trading Boundary
(illustrative)
Energy is bought and sold at the Trading Boundary.
As a result of losses, “X” MW bought in BETTA becomes (X*0.987) MW which the Participant is paid for in SEM.
As the TLAF (=CLAF) is calculated based on importing, this treatment is correct.
X MW
(X * 0.987) MW
(X * 0.987) MW
Notes: *
*
<number>##

## Slide 10: Loss Adjustment in the SEM - Exporting
<number>
Trading Boundary
(illustrative)
As a result of losses, “X * 0.987” MW is bought at the SEM Trading Boundary by the PT and is paid for “X” MW in BETTA.
This is incorrect as there is an imbalance between what the Participant buys in SEM and what the Participant is paid for in BETTA
X MW
(X / 0.98) MW
(X / 0.98) MW
X MW
(X * 0.987) MW
(X * 0.987) MW
Notes: *
*
<number>##

## Slide 11: Examples of current calculations
<number>
For an importing Interconnector Unit:
  If Ex-Post MSQ = +80MW.
  User is paid for [80MW * 0.9 = 72MW] from SEM and has purchased 80MW from BETTA.
  As CLAF<1, the User is being paid for less energy in SEM than it is being paid for in BETTA, i.e. reflecting the effects of losses.
For an exporting Interconnector Unit:
  If Ex-Post MSQ = -80MW.
  User buys [80MW * 0.9 = 72MW] from SEM and delivers 80MW to BETTA.
  As CLAF<1, the User is purchasing less energy in SEM that is being delivered to BETTA, i.e. not reflecting impacts of losses.
Notes: *
*
<number>##

## Slide 12: Resolving the Loss Adjustment Error when an Interconnector is Exporting
<number>
Option 1 : One TLAF
    One TLAF would continue to be determined by TSOs for Interconnectors, based on the forecast pre-dominant direction of flow.
    This TLAF would continue to be provided to the settlement system.
    Loss adjustment would be by CLAF or (1/CLAF), depending on the sign convention of the relevant MW quantity (e.g. MSQ, DQ, MG etc):
      CLAF when the quantity is > 0
      (1/CLAF) when the quantity is < 0
Notes: *
*
<number>##

## Slide 13: Resolving the Loss Adjustment Error when an Interconnector is Exporting
<number>
Option 2 : Two TLAFs
    Two TLAFs would be determined by TSOs for Interconnectors: one for import and one for export.
    These would be submitted using the existing interface feed (amended to allow two TLAFs for Interconnectors).
    Two TLAFs would be provided to the settlement system.
    TLAFs would be applied based on the sign of the relevant MW quantity (e.g. MSQ, DQ, MG etc):
      Importing CLAF for when the quantity is > 0
      Exporting CLAF for when the quantity is < 0
Notes: *
*
<number>##