## Slide 1: MOD_17_12
Report on Offered Capacity in
Implicit Auctions

## Slide 2: Proposed Change
New report on the Offered Capacity in Implicit Auctions identifying Interconnector trading opportunities in EA2 and WD1
Required by Congestion Management Guidelines [Regulation (EC) no. 714/2009]
Consistent with SEM-12-054 [Intra Day Congestion Charging Methodology]
To be produced after EA2 and WD1, for each Interconnector, for each Trading Period

## Slide 3: Report Content
Indication of the minimum IUN allocation available in any Trading Period
Total
MIUNs
Total
MIUNs
Import Offered Capacity
Export Offered Capacity
0
Import ATC
Export ATC
TP1
TP2

## Slide 4: T&SC Drafting Change
Changes made to IDT version of the code [MOD_18_10 V2]
Added reports to Appendix E and Agreed Procedure 6
New Terms in Glossary
  AIC: Allocated Interconnector Capacity
  OICE: Implicit Auction Offered Interconnector Capacity for Export
  OICI: Implicit Auction Offered Interconnector Capacity for Import

## Slide 6: MOD_18_12
Constraint Payments Calculation for Interconnector Residual Capacity Units

## Slide 7: Proposed Change 1
Mod_12_11: Interconnector Unit Loss Adjustment when Exporting
  Original: XXXLFuh = XXXuh x CLAFuh
  Import: XXXLFuh = XXXuh x CLAFuh
  Export: XXXLFuh = XXXuh / CLAFuh
This Mod is to treat Interconnector Residual Capacity Units in the same way:
  Interim: CONPuh = (SIIPlh + SIEPlh) * CLAFuh
  Proposed: CONPuh = (SIIPlh x CLAFuh) + (SIEPlh / CLAFuh)

## Slide 8: Proposed Change 2
Simplification of the Calculation
  Current: CONPuh = (SIEPlh x SIEQlh + SIIPlh x SIIQlh) x TPD x CLAFuh
  Interim: CONPuh = (SIIPlh + SIEPlh) * CLAFuh
  Proposed: CONPuh = (SIIPlh x CLAFuh) + (SIEPlh / CLAFuh)
Current: notional hourly price by quantity in a given direction
Proposed: half hourly net payment information
Multiply the import payment by CLAF and divide the export payment by CLAF
Allows for more complex SO Trade scenarios

## Slide 9: SO Trade – details for reference
An SO Trade can only occur after market gates are completed for the relevant Trading Periods
Paper due to be published shortly explicitly detailing the scenarios where they will be considered
New reports being introduced on the Auction Management Platform
  SO Trade Prices
  Individual SO Trade details

## Slide 10: T&SC Drafting Change
Changes to definitions in 5.70, Glossary, Appendix K, e.g.
  SO Interconnector Import Price Payment (SIIPlh) which is the volume-weighted average pricepayment for each Trading Period for SO Interconnector Trades which are forwhen they are a net MW import to the Pool (or zero if there are no such trades);
  SO Interconnector Import Quantity (SIIQIh) which is the time-weighted average net quantity for each Trading Period (expressed as a positive number in MW) of SO Interconnector Trades which are forwhen they are a net MW import to the Pool (or zero if there are no such trades)
Calculation in 5.90 changed as previous (proposed) and the interim calculation in 7.70
  Implementation with Mod_12_11

## Slide 11: Systems
Source system for the SO Trade information is the Auction Management Platform
No change to SEM interfaces – uses existing SO Interconnector Trade Data Transaction
Calculation performed by SEMO Operations for invoicing using spreadsheet (minor adjustment)