## Slide 1: Intra Day Trading : Working Group 7 16 November 2010
Notes: *
*
<number>##

## Slide 2
Agenda
Introduction – Recap of Working Group 6
Approval Process
Design Discussion
- Data Contingencies – Active Capacity Holdings
- Interconnector Units: Credit Cover
- TSO Security Options
High Level Design
Recap
- Agreed Recommendations
- Actions
Notes: <number>

## Slide 3
Working Group #6 discussed a number of issues:
Intra-Day Trading design:
  Fixed/Superposition vs. Protection Working Assumption: Fixed/Superposition
  Data Transaction Contingencies SEMO to consider Active Capacity Holdings
  MSP Software Run Contingencies Working Assumption: Option 2(b)
  Trading Windows & Optimisation Time Horizons Working Assumptions:
      1) 30 hour WD1 Optimisation Time Horizon
      2) WD1 Trading Window starts at 18:00
  Credit Management 1) Working Assumption: Hybrid Option 1A
  2) SEMO to consider Capacity Credit Cover options
Market Schedule Production Process:
  As per previous action, SEMO has provided a summary of the Market Schedule production process
  SEMO believes that the 90 minute process is challenging but achievable
Implementation Timescales
  SEMO explained current implementation timescales and impacts on scheduled releases
Approval Process
  RA Chair explained the process by which intra-day will be approved
  Once there are working assumptions on all key issues, a High Level Design document will be issued to the Modifications Committee for discussion and vote at meeting #32 (25 Nov 2010)
  This High Level Design document will then be considered by the SEM Committee (30 Nov 2010)
Notes: <number>

## Slide 4
Agenda
Introduction – Recap of Working Group 6
Approval Process
Design Discussion
- Data Contingencies – Active Capacity Holdings
- Interconnector Units: Credit Cover
- TSO Security Options
High Level Design
Recap
- Agreed Recommendations
- Actions
Notes: <number>

## Slide 5
WG5
05 Oct 2010
Conf Call 3
26 Oct 2010
WG6
02 Nov 2010
WG7
16 Nov 2010
Mod Expiry
16 Nov 2010
High Level Design Summary
submitted to Mods Committee
18 Nov 2010
Mods Committee 32 Decision
25 Nov 2010
SEMC Meeting
30 Nov 2010
SEMC Meeting
25 Jan 2011
Summary of Approval Process
Now
Notes: <number>

## Slide 6
Agenda
Introduction – Recap of Working Group 6
Approval Process
Design Discussion
- Data Contingencies – Active Capacity Holdings
- Interconnector Units: Credit Cover
- TSO Security Options
High Level Design
Recap
- Agreed Recommendations
- Actions
Notes: <number>

## Slide 7
Data Transaction Contingencies
Active Capacity Holdings
Notes: <number>

## Slide 8
In line with Option 2 timelines, key timings for Trading Day TD are:
Timings with Intra-Day Trading
08:00
WD1
GWC
(TD)
09:30
WD1
Schedule
(TD)
09:30
EA1
GWC
(TD-1)
11:00
EA1
Schedule
(TD-1)
11:30
EA2
GWC
(TD-1)
13:00
EA2
Schedule
(TD-1)
13:00
RCUC DA
GWC
(TD-1)
16:00
RCUC DA
Schedule
(TD-1)
The clustering of Gate Windows could result in delays and issues if key data is not available.
Contingency data is therefore required for TSO/IA Data Transactions for when data is not received by the relevant Gate Window Closure (note that this is only relevant for Ex-Ante Runs EA1, EA2 and WD1).
09:30
RCUC WD
GWC
(TD)
RCUC WD
Schedule*
(TD)
* TSOs to confirm the timescales for the delivery of the within day Operations Schedule
Notes: <number>

## Slide 9
Proposed Contingency Data: MSP Software Runs
Data Transaction | EA1 | EA2 | WD1
Four Day Load Forecast | Most recent Four Day Load Forecast Accepted by the relevant Gate Window Closure | Most recent Four Day Load Forecast Accepted by the relevant Gate Window Closure | Most recent Four Day Load Forecast Accepted by the relevant Gate Window Closure
Wind Power Unit Forecast | Most recent Wind Forecast Accepted by the relevant Gate Window Closure | Most recent Wind Forecast Accepted by the relevant Gate Window Closure | Most recent Wind Forecast Accepted by the relevant Gate Window Closure
Interconnector Available Transfer Capacity | Most recent ATC data Accepted by the relevant Gate Window Closure | Most recent ATC data Accepted by the relevant Gate Window Closure | Most recent ATC data Accepted by the relevant Gate Window Closure
Active Interconnector Capacity Holdings | If not received via CMS, faxed and emailed by IA to SEMO. If not received or available, zeros will be used. |  | 
Modified Interconnector Unit Nominations |  | IUNs if available from the EA1 MSP Software Run. If not, zeros will be used. | MIUNs if available from the EA2 MSP Software Run. If not, IUNs if available from the EA2 MSP Software Run. MIUNs if available from the EA1 MSP Software Run. If not, IUNs if available from the EA1 MSP Software Run. Otherwise, zeros will be used.
WG6 Working assumption on all contingencies except for Active Capacity Holdings
Notes: <number>

## Slide 10
Suggestion 1: Utilise longer term capacity auction information for the Trading Day (e.g. annual, monthly)
There is no mechanism for the submission, storage or use of Annual or Monthly Capacity Holdings within the Central Market Systems. If implemented, it could have a significant cost to deal with an event that is extremely unlikely (no systems, no fax and no email).
There would be SEMO resource impacts if a manual process to input this data was implemented (this would also need to include the development of desk procedures, checking etc). In addition SEMO is obliged to comply with Trading and Settlement Code clause 3.46:
“The Market Operator shall not estimate or substitute System Operator Market Data Transactions, Interconnector Administrator Market Data Transactions or Meter Data Transactions except as required when Administered Settlement is in effect.”
SEMO believes that any manual process would be impractical, given the compacted Gate Window and MSP Software Run timelines proposed for Intra-Day trading. It would also create audit issues.
Alternate suggestions raised at Working Group 6 (1)
Notes: <number>

## Slide 11
Suggestion 2: Allow Participants to submit Active Capacity Holdings
SEMO believes that this would compromise the obligations within the Code and could result in issues where the Participant-submitted values do not correspond with the IA-submitted values.
If implemented, new interfaces, validations and logic would be required (in CMS and Participant systems). This would affect all Participants, not simply Interconnector Users.
Alternate suggestions raised at Working Group 6 (2)
Notes: <number>

## Slide 12
It is likely to be extremely rare (it would require systems, fax and email all to be unavailable) and would likely cause much more disruption than simply to Capacity Holders.
Any change could have significant cost, to CMS, IA and Participant systems.
SEMO therefore proposes that the following should be progressed as the working assumption for the High Level Design for Intra-Day Trading:
In the event that Active Capacity Holding data is not received within the CMS from the IA for a particular Trading Day,
  The IA will fax and email the data to SEMO.
  If no data can be provided (which could, in effect, only occur in the highly unlikely event there was a power failure in the IA’s offices and any back-up generator also failed), the Active Capacity Holdings will be set to zero.
Discussion and SEMO proposal
Notes: <number>

## Slide 13
Credit Risk Management (CRM)
Notes: <number>

## Slide 14
As suggested at the last Working Group, only the export components of bids rejected after Gate Closure if insufficient Credit Cover in place:
Updates to agreed Working Assumption on Credit Cover for Interconnector Units
Offered
The maximum export exposure (in respect of Energy Charges) is implied by a set of Price Quantity Pairs submitted to a particular Gate Window (export component rejected after Gate Window Closure if insufficient Credit Cover in place).
Additional calculation of Capacity Credit Cover, based on a similar methodology to the current approach and that agreed for Energy at WG6:
  Forecast Capacity Price * Volume
    Net if Capacity is settled or EP2 (Energy Market) is settled
    Based on maximum exposure where EP2 not completed
Notes: <number>

## Slide 15
Proposed Design: Elements of Credit Exposure Calculation
(Energy Market)
Invoiced
Settled
Traded
Now
Amounts invoiced and payment outstanding (netted)
Amounts calculated but not yet invoiced (netted)
Offered
Invoiced
Settled
Traded
Offered
Where:
Amounts calculated based on traded values where not Settled (i.e. between D+1 and D+4), based on export MIUNs and PQ Pairs Accepted.
The maximum export exposure (in respect of Energy Charges) is implied by a set of Price Quantity Pairs submitted to a particular Gate Window (export component rejected after Gate Window Closure if insufficient Credit Cover in place).
7 days
7 days
Notes: <number>

## Slide 16
Proposed Design: Elements of Credit Exposure Calculation
(Capacity Market) - 1
Invoiced
Settled
Traded
(Energy Settled)
Now
Amounts invoiced and payment outstanding (netted)
Amounts calculated but not yet invoiced (netted)
Offered
Invoiced
Settled
Traded
(Energy Settled)
Where:
Capacity amounts calculated based on net traded volumes where Capacity is not Settled (i.e. Initial Capacity Settlement is not completed) but the Initial Energy Settlement is completed, using the forecast Capacity Payments Generation Price, CPGP (netted).
Note: As Capacity Payments/Charges are settled on a monthly basis, the length of the Invoiced, Settled and Traded periods will depend on the day on which the Credit Cover calculation is performed (this is the same as the current market design).
Traded (Energy
Not Settled)
Notes: <number>

## Slide 17
Proposed Design: Elements of Credit Exposure Calculation
(Capacity Market) - 2
Invoiced
Settled
Traded
(Energy Settled)
Now
Offered
Traded
(Energy Not Settled)
Offered
Where:
Amounts calculated based on export traded volumes where Capacity is not Settled (i.e. where Initial Capacity Settlement has not been completed) and where Initial Energy Settlement is not complete, based on the Quantities as part of a set of Price Quantity Pairs submitted to a particular Gate Window and a forecast Capacity Payments Generation Price.
The maximum exposure (in respect of Capacity Charges) is as implied by the Forecast Capacity Payments Generation Price and the export Quantity as part of a set of Price Quantity Pairs submitted to a particular Gate Window (bids implying export would be rejected after Gate Window Closure if insufficient Credit Cover in place, however bids implying import would be retained).
Note: As Capacity Payments/Charges are settled on a monthly basis, the length of the Invoiced, Settled and Traded periods will depend on the day on which the Credit Cover calculation is performed (this is the same currently).
Traded (Energy
Not Settled)
Notes: <number>

## Slide 18
Proposed Design: Calculation of Potential “Traded” Capacity Market Exposure
* The forecast CPGP will be calculated in the same way the Estimated Capacity Price (ECP), based on data for the Historical Assessment Period at the 95th percentile.
Traded
(Energy Settled)
Capacity amounts calculated based on net traded volumes where Initial Energy has been settled but Initial Capacity has not been Settled. Uses the forecast Capacity Payments Generation Price (CPGP).
0
P
Q
EA1_MIUN
EA2_MIUN
WD1_MIUN
For each Trading Period in the MSP Software Runs that have been completed when the Credit Cover calculation is executed:
Maximum Capacity Market exposure is based on the relevant MIUN and the forecast Capacity . This is the shaded area (which may be positive or negative).
Forecast CPGP *
Notes: <number>

## Slide 19
Proposed Design: Calculation of Potential “Traded” Capacity Market Exposure
* The forecast CPGP will be calculated in the same way the Estimated Capacity Price (ECP), based on data for the Historical Assessment Period at the 95th percentile.
Traded (Energy
Not Settled)
Amounts calculated based on traded export volumes (not netted) where both Initial Energy settlement and Initial Capacity settlement have not been completed. Credit Cover is based on the MIUNs allocated in EA1, EA2 and WD1 MSP Software Runs, and a forecast Capacity Payments Generation Price.
For each Trading Period in the MSP Software Runs that have been completed when the Credit Cover calculation is executed:
0
P
Q
The maximum “Traded (Energy Not Settled)” Capacity Market potential exposure is based on the relevant MIUN and the forecast Capacity Payments Generation Price. This is the shaded area.
Proposed design requires Interconnector traders to have sufficient Credit Cover in place (to cover both Energy and Capacity exposure), otherwise bids implying export will be excluded following the relevant Gate Window Closure.
EA1_MIUN
EA2_MIUN
WD1_MIUN
Forecast CPGP *
Notes: <number>

## Slide 20
Proposed Design: Calculation of “Offered”
Capacity Market Exposure
Within each Ex-Ante Gate Window:
The maximum Capacity Market potential exposure is the maximum export Quantity multiplied by the forecast Capacity Payments Generation Price (CPGP). This is the shaded area.
Proposed design requires Interconnector traders to have sufficient Credit Cover in place (to cover both Energy and Capacity exposure), otherwise bids implying export will be rejected following the relevant Gate Window Closure.
Offered
The maximum exposure implied by the Quantities from a set of Price Quantity Pairs submitted to a particular Gate Window (rejected after Gate Window Closure if insufficient Credit Cover in place) and the forecast Capacity Payments Generation Price (CPGP):
0
P
Q
P1Q1
P2Q2
P4Q4
P3Q3
Forecast CPGP *
Max(Qi)
* The forecast CPGP will be calculated in the same way the Estimated Capacity Price (ECP), based on data for the Historical Assessment Period at the 95th percentile.
Notes: <number>

## Slide 21
TSO Security Options
Notes: <number>

## Slide 22
Agenda
Introduction – Recap of Working Group 6
Approval Process
Design Discussion
- Data Contingencies – Active Capacity Holdings
- Interconnector Units: Credit Cover
- TSO Security Options
High Level Design
Recap
- Agreed Recommendations
- Actions
Notes: <number>

## Slide 23
In parallel with the Working Group process, SEMO has been developing the Intra-Day Trading: High Level Design document.
As per the Intra-Day timeline (provided at each meeting), this document will be submitted to Modifications Committee meeting #32 (25 November 2010).
It is expected that the High Level Design document will be issued by 18 November 2010 to Modifications Committee and Working Group members.
The Modifications Committee will vote on the principles as set out in the High Level Design document.
The High Level Design will then be presented to the SEM Committee (30 November 2010), proposing that the principles are accepted for further development in the Detailed Design phase.
High Level Design
Notes: <number>

## Slide 24
Introduction
Overview
Design Summary
  Gate Windows
  Trading Windows
  Optimisation Time Horizons
  Participant External Data Inputs
    Commercial Offer Data
    Technical Offer Data / Registration Data
    Default Data / Starting Gate Window Data
    Non-Participant External Data Inputs
    Interfaces with System Operators
  Interfaces with Interconnector Administrators
  Interfaces with Meter Data Providers
  Data Contingencies
  Market Operator Data Inputs
    Treatment of Trading Day Exchange Rate
High Level Design – document structure (1)
Notes: <number>

## Slide 25
Design Summary (continued)
  MSP Software Runs
    Modelling of Loading Rates and Notification Times in the MSP Software
    Ex-Ante Indicative MSP Software Run 1 (EA1)
    Ex-Ante Indicative MSP Software Run 2 (EA2)
    Within-Day MSP Software Run (WD1)
    Ex-Post Indicative MSP Software Run (EP1)
    Ex-Post (Initial) MSP Software Run (EP2)
    MSP Software Run Cancellation and Contingency
  Impact of Reduction in Interconnector Capacity
    Reductions in ATC
    Increases in ATC
  Publication and Reporting
  Settlement
  Credit Management
    Current Credit Cover in the SEM
    Current Credit Cover for Interconnector Units
    Credit Cover for Interconnector Units under Intra-Day Trading
  Invoicing
  Funds Transfer
Appendix A – Glossary
Appendix B - Configurability
  Introduction
  Key Terms
  Configurability Summary
High Level Design – document structure (2)
Notes: <number>

## Slide 26
Agenda
Introduction – Recap of Working Group 6
Approval Process
Design Discussion
- Data Contingencies – Active Capacity Holdings
- Interconnector Units: Credit Cover
- TSO Security Options
High Level Design
Recap
- Agreed Recommendations
- Actions
Notes: <number>