## Slide 1
Trading & Settlement Code modification
Mod 21 / 12
Amendment to Available Transfer Capacity (ATC) definition

## Slide 2
At present the Trading and Settlement Code limits any changes in the Maximum Export and Import Available Transfer Capacities to causes associated only with the Interconnector equipment.
“5.42 Maximum Import Available Transfer Capacity shall relate to the physical capability of the Interconnector to deliver energy to the Transmission System, and shall take account of any further restrictions placed by any relevant agreement or the provisions of any Licence in respect of the Interconnector, but shall not otherwise take account of any expected transmission constraints or other aspects of the operation of the Transmission System.”
5.42 Maximum Import Available Transfer Capacity shall relate to the physical capability of the Interconnector to deliver energy to the Transmission System, and shall take account of any further restrictions placed by any relevant agreement, the applicable transfer capacity determination procedure or the provisions of any Licence in respect of the Interconnector, but shall not otherwise take account of any expected transmission constraints or other aspects of the operation of the Transmission System.
Same change for 5.43 the export capacity clause
Modification

## Slide 3
Interconnection and System Security
Interconnector transfer capacity determination process
TSC Modification
NTC / ATC terminology discussion

## Slide 4
One of the prime obligations of TSOs is to operate the power system in a secure manner
Includes managing the effects that inter-jurisdictional interconnector flows have on the power system
Regulation (EC) No. 714/2009 as stated in article 1:
(16) The precondition for effective competition in the internal market in electricity is non- discriminatory and transparent charges for network use including interconnector lines in the transmission system. The available capacity of those lines should be set at the maximum levels consistent with the safety standards of secure network operation.
Full transfer capacity between jurisdictions may be limited at times, depending on interconnector equipment and the connecting transmission systems
The facility for TSOs to determine and set transfer limits on inter-jurisdictional flow to respect security standards is required to ensure the secure operation of the transmission system
Interconnection and System Security

## Slide 5
Interconnector Transfer capacity
Ireland power system
GB power system
Interconnector equipment
Transfer Capacity
calculated for export and import from/ to connection point respecting security standards
Transfer Capacity
calculated for flow in either direction
TTC in direction
for the interconnector is the minimum of
Ireland system export capacity
interconnector equipment
GB system import capacity
Transfer Capacity
calculated for export and import from/ to connection point respecting security standards
TTC in direction
for the interconnector is the minimum of
Ireland system import capacity
interconnector equipment
GB system export capacity
Interconnection and System Security

## Slide 6
The TSOs have developed an interconnector transfer capacity determination process for the East West interconnector which has been reviewed by the Regulatory Authorities and published
Required under Regulation (EC) No 714/2009
(conditions for access to the network for cross-border exchanges in electricity) Annex 1 (5.2)
5.2. TSOs shall publish a general description of the congestion-management method applied under different circumstances for maximising the capacity available to the market, and a general scheme for the calculation of the interconnection capacity for the different timeframes, based upon the electrical and physical realities of the network. Such a scheme shall be subject to review by the regulatory authorities of the Member States concerned.
An Interconnector capacity calculation document exists for the Moyle Interconnector which documents the determination of transfer limits and will be developed to include a curtailment process to align with the East West process document
Interconnector capacity adjustment is used throughout Europe to communicate, co-ordinate and invoke transfer limitations between control areas to maintain system security
Interconnection and System Security

## Slide 7
The three key objectives of the capacity calculation process are to -
ensure that any energy flows on the Interconnector do not undermine the secure operation of the power systems in Great Britain and Ireland
maximise the amount of capacity made available on the Interconnector for market participants to trade energy
give participants confidence that curtailment of any scheduled energy flows by the System Operator would only occur in exceptional circumstances
PROCESS FOR DETERMINING TRANSFER CAPACITY ON THE EAST WEST INTERCONNECTOR

## Slide 8
ENTSO-E: Total Transfer Capacity TTC is the maximum exchange programme between two areas compatible
with operational security standards applicable at each system if future network conditions,
generation and load patterns were perfectly known in advance.
ENTSO-E: Transmission Reliability Margin TRM is a security margin that copes with uncertainties on the computed TTC values arising from:
Unintended deviations of physical flows during operation due to the physical functioning of load-frequency regulation
Emergency exchanges between SOs to cope with unexpected unbalanced situations in real time
Inaccuracies, e.g. in data collection and measurements
ENTSO-E: Net Transfer Capacity is defined as NTC = TTC - TRM and corresponds to the maximum exchange between two areas compatible with security standards applicable in both areas and taking into account the technical uncertainties on future network conditions.
ENTSO-E: Already Allocated Capacity AAC is the total amount of allocated transmission capacity rights, whether they are capacity or exchange programmes depending on the allocation method.
ENTSO-E: Available Transmission Capacity is the part of NTC that remains available, after each phase of the allocation procedure, for further commercial activity. ATC is given the following equation: ATC = NTC – AAC.
NTC - refers to the link capability, taking account of transmission constraints
ATC - refers to remaining capacity available for explicit and implicit auctions
PROCESS FOR DETERMINING TRANSFER CAPACITY ON THE EAST WEST INTERCONNECTOR

## Slide 9
Potential NTC restrictions
The NTC on EWIC will be set to 0 MW for any outages of the Interconnector or associated connection assets.
NTC reductions can also occur where transfers on the Interconnector result in breaches of operational security of the transmission systems in either Great Britain or Ireland.
The power systems on both sides of EWIC are robust and such system security induced transfer capacity restrictions would only occur in exceptional circumstances involving unplanned outages of critical transmission and generation infrastructure.
As prudent system operators the TSOs must perform studies to assess the impact of all planned and unplanned outages of the transmission system on the transfer capacity of EWIC.
PROCESS FOR DETERMINING TRANSFER CAPACITY ON THE EAST WEST INTERCONNECTOR

## Slide 10
Timing
NTC studies are primarily done to inform the capacity allocation process and as such must be done in the timeframes required by this process.
Annual studies
Six-monthly studies.
Monthly.
Daily. Carried out on D-2 to support the D-1 auction process and Day Ahead SEM runs
In-day. Carried out as required in-day if system conditions deviate from forecast.
PROCESS FOR DETERMINING TRANSFER CAPACITY ON THE EAST WEST INTERCONNECTOR

## Slide 11
Changes in NTC between allocation phases
The TSO should ensure that the capacity offered in the auction phases is compatible with system security in order to avoid scheduled transactions being curtailed in real time.
This objective must be balanced by the need to make as much capacity available to the market as is reasonably practicable. When calculating NTC before a capacity auction (or implicit allocation) takes place the TSO will use the most up-to-date information available to perform the calculations.
Changes in forecasted system conditions can result in changes to NTC values between capacity auction phases.
NTC changes can be driven by outages of the Interconnector or by changes in forecasted system conditions.
PROCESS FOR DETERMINING TRANSFER CAPACITY ON THE EAST WEST INTERCONNECTOR

## Slide 12
Changes in NTC between allocation phases
Changes in NTC driven by outages of the Interconnector
Any change in the availability of EWIC will result in an immediate change in NTC regardless of the timeframe in which this takes place.
Changes in NTC driven by NGET
Any NTC reduction imposed by NGET for system security requirements on the NGET power system will be implemented in the same way as NTC reductions driven by system security requirements on the EirGrid system.
PROCESS FOR DETERMINING TRANSFER CAPACITY ON THE EAST WEST INTERCONNECTOR

## Slide 13
PROCESS FOR DETERMINING TRANSFER CAPACITY ON THE EAST WEST INTERCONNECTOR
Changes in NTC between allocation phases
Changes in NTC driven by system security requirements
Changes in NTC before SEM Ex-Ante 1 Gate Closure
The TSOs will re-calculate the NTC for each allocation phase up to gate closure. If the calculated NTC is less than any Already Allocated Capacity (AAC) then the NTC will be set to the recalculated value and capacity holders will be refunded the costs of any capacity withdrawn from them per the EWIC access rules.
Changes in NTC between SEM Ex-Ante 2 Gate Closure and Final Gate Closure
For a change in forecasted system conditions the TSOs will re-calculate the NTC for each gate closure. If the calculated NTC is less than the net scheduled transactions from the previous Gate then the NTC will be set to the value of the net scheduled transaction for the next gate closure. For example, if the export NTC is calculated as 300MW but 350MW export is the net scheduled transaction in the Ex-Ante 1 run then the NTC will be set at 350MW for the Ex-Ante 2 run. If the final set of scheduled transactions (set by EA2 for 6:00-17:30 and Within Day 1 for 18:00-5:30) exceeds the calculated NTC the post gate closure curtailment process will be applied if necessary
Changes in NTC after Final Gate Closure
If the newly calculated NTC is less than the net scheduled transactions the post gate curtailment process will be applied in real time operation to try and ensure that any scheduled flow takes place securely.

## Slide 14
PROCESS FOR DETERMINING TRANSFER CAPACITY ON THE EAST WEST INTERCONNECTOR
post gate curtailment PROCESS
Interconnector flow curtailment will only occur in exceptional circumstances (i.e. as a last resort) and will be applied in a non discriminatory manner.
Energy transactions scheduled in the SEM Within Day 1 gate are curtailed before energy transactions scheduled in Ex-Ante 2. Ex-Ante 2 scheduled transactions are curtailed before Ex-Ante 1
Within each of these gates, curtailment is executed on a pro-rata basis across all participants.
The types of events that can give rise to curtailment include:
Interconnector faults (i.e. where the Interconnector equipment cannot physically deliver or receive Interconnector transfers)
Loss of transmission capacity in Ireland or Great Britain, such that all remedial actions, generation re-dispatch, counter trading and emergency assistance options have been exhausted and the transmission system cannot maintain the planned Interconnector transfers securely
Capacity shortfalls in Great Britain or Ireland, where generation or demand side actions are insufficient to meet the system demand, operating reserve requirements and Interconnector transfers

## Slide 15
PROCESS FOR DETERMINING TRANSFER CAPACITY ON THE EAST WEST INTERCONNECTOR
post gate curtailment PROCESS
Before reducing energy flow on the Interconnector the TSO must:
Utilise remedial actions including the re-dispatch of generation or demand side plant to relieve the security constraint, if possible
Counter-trade to reduce Interconnector flows, if available
Utilised SO/SO Emergency Assistance
In the event that these actions are ineffective the TSO will reduce the energy flow and re-declare the NTC. This process is consistent with the requirements of EU Regulation (EC) No 714/2009 Article 16 (2).

## Slide 16
The ability for System Operators to curtail interconnector flows is enshrined in regulation (EC) No. 714/2009 as stated in article 16:
General principles of congestion management
2. Transaction curtailment procedures shall only be used in emergency situations where the transmission system operator must act in an expeditious manner and re-dispatching or countertrading is not possible. Any such procedure shall be applied in a non-discriminatory manner. Except in cases of force majeure, market participants who have been allocated capacity shall be compensated for any curtailment.
Curtailment

## Slide 17
Regulation (EC) No 714/2009 Annex 1 part 2.13 states that the financial consequences of curtailing capacity falls to those who are responsible for such a failure.
2.13 The financial consequences of failure to honour obligations associated with the allocation of capacity shall be attributed to those who are responsible for such a failure. Where market participants fail to use the capacity that they have committed to use, or, in the case of explicitly auctioned capacity, fail to trade on a secondary basis or give the capacity back in due time, they shall lose the rights to such capacity and pay a cost-reflective charge. Any cost-reflective charges for the non-use of capacity shall be justified and proportionate. Likewise, if a TSO does not fulfil its obligation, it shall be liable to compensate the market participant for the loss of capacity rights. No consequential losses shall be taken into account for that purpose. The key concepts and methods for the determination of liabilities that accrue upon failure to honour obligations shall be set out in advance in respect of the financial consequences, and shall be subject to review by the relevant national regulatory authority or authorities.
Market Participants will be compensated for loss of capacity rights in the event of a transmission restriction being imposed on interconnector capacity in line with the compensation mechanism set out in the interconnector Access Rules.
Compensation

## Slide 18
At present the Trading and Settlement Code limits any changes in the Maximum Export and Import Available Transfer Capacities to causes associated only with the Interconnector equipment.
“5.42 Maximum Import Available Transfer Capacity shall relate to the physical capability of the Interconnector to deliver energy to the Transmission System, and shall take account of any further restrictions placed by any relevant agreement or the provisions of any Licence in respect of the Interconnector, but shall not otherwise take account of any expected transmission constraints or other aspects of the operation of the Transmission System.”
5.42 Maximum Import Available Transfer Capacity shall relate to the physical capability of the Interconnector to deliver energy to the Transmission System, and shall take account of any further restrictions placed by any relevant agreement, the applicable transfer capacity determination procedure or the provisions of any Licence in respect of the Interconnector, but shall not otherwise take account of any expected transmission constraints or other aspects of the operation of the Transmission System.
Same change for 5.43 the export capacity clause
Modification

## Slide 19
Appendix K 21
Modification
Sender | Interconnector Administrator
Recipient | Market Operator
Number of Data Transactions | One containing: In all cases, for the relevant Interconnector, Maximum Import Available Transfer Capacity and Maximum Export Available Transfer Capacity for each Trading Period in the relevant Optimisation Time Horizon. Only in the event that the relevant Interconnector Available Transfer Capacity has desynchronised unexpectedly changed, values and associated time for each change in Maximum Import Available Transfer Capacity or Maximum Export Available Transfer Capacity within the relevant Trading Day.
Frequency of Data Transactions | Daily and as updated
First Submission time | As available
Last Submission time | Unlimited, at least one Data Transaction shall be submitted by 10:00 on the day prior to the EA1 Gate Window Closure
Table K.30 – Interconnector Available Transfer Capacity Data Transaction Submission Protocol

## Slide 20
ENTSO-E: Total Transfer Capacity TTC is the maximum exchange programme between two areas compatible
with operational security standards applicable at each system if future network conditions,
generation and load patterns were perfectly known in advance.
ENTSO-E: Transmission Reliability Margin TRM is a security margin that copes with uncertainties on the computed TTC values arising from:
Unintended deviations of physical flows during operation due to the physical functioning of load-frequency regulation
Emergency exchanges between SOs to cope with unexpected unbalanced situations in real time
Inaccuracies, e.g. in data collection and measurements
ENTSO-E: Net Transfer Capacity is defined as NTC = TTC - TRM and corresponds to the maximum exchange between two areas compatible with security standards applicable in both areas and taking into account the technical uncertainties on future network conditions.
ENTSO-E: Already Allocated Capacity AAC is the total amount of allocated transmission capacity rights, whether they are capacity or exchange programmes depending on the allocation method.
ENTSO-E: Available Transmission Capacity is the part of NTC that remains available, after each phase of the allocation procedure, for further commercial activity. ATC is given the following equation: ATC = NTC – AAC.
NTC - refers to the link capability, taking account of transmission constraints
ATC - refers to remaining capacity available for explicit and implicit auctions
ATC / NTC

## Slide 21
Interconnector Transfer capacity
Interconnector Owner
Interconnector Administrator
AMP
TSO
SEMO
capacity (NTC)
Interconnector
users
capacity (ATC)
appointed role
agreement
ATC / NTC