## Slide 1: Mod_03_18 Version 3 Autoproducer & DSU Credit Cover Thomas O’Sullivan 5 Dec 2019

## Slide 2: Working Group Mod_03_18 timeline
Jan 2018 original proposal Meeting 79
Affects DSU as well as Autoproducer
Agreed to set up Working Group
Agreed to put short term measures in place
Mar 2018 interim solution proposed Mod_09_18 Meeting 81
Effective date 27 Aug 2018
Working Group Mod _03_18
Meeting 1 Jan to May 2019
Presentation 27 June Meeting 92
Mod_03_18 Version 3 today 5 Dec 2019 Meeting 95

## Slide 3: Problem refined
Credit Requirement for Defined Exposure Period
No issue with TSC
Credit Requirement for Undefined Exposure Period
Settlement under the TSC combines 1)Generation and 2)Demand for Autoproducers and for DSU
Collateral Undefined Exposure Period, under the TSC, independently assess 1)historical generation cash flow and 2) historical demand metered quantity
The Working Group agreed the TSC as it stands produces excess collateral requirements

## Slide 4: Materiality Self Assessment
Autoproducer:
€ 949k calculated by Aughinish
Additional € 400k to 700k if Supplier suspension delay period is changed.
DSU:
Normal exposure of € 1,000,000
Max exposure could be up to € 4,100,000
Huge additional cost if Supplier suspension delay period is changed

## Slide 5: Mod_03_18 Version 3
Version 3 is new - please disregard any previous version
Maintains the intent
Eliminates additional variables
Less software changes
Better transparency
Cash flow for TSSUs when calculating EUPEG (Undefined Potential Exposure for Trading Payments)
It enables two variants of Billing Period Metered Demand, QMB for a participant:
  in respect of any TSSUs
  all other Supplier Units
Addresses the issues :
  New and Adjusted Participant
  Settlement Reallocation Agreement

## Slide 6: Mod_03_18 Version 3
Billing Period Cashflow (CUB)
Historical cash flow now includes all units within a DSU or Autoproducer portfolio

## Slide 7: Mod_03_18 Version 3
Supplier Billing Period Metered Demand, QMB
No No favorable treatment for a Trading Site when consuming power:
Quantity same as a SU
Imperfection price is same
Capacity exposure is same
Generator outage, consumption of 10MW

## Slide 8: Mod_03_18 Version 3
Dialog:
Version 3 solves all material issues raised by the proposer
Version 3 solves new issues:
  DSU
  New and Adjusted Participant
  Settlement Reallocation Agreement
Version 3 is more transparent
Version 3 is more efficient

## Slide 9: Aughinish Recommendation
Any future code modification of Supplier Suspension Delay Period should consider exempting Trading Site Supplier Units registered as part of an Autoproducer Site or registered as part of a DSU .
Approve Version 3 of Mod_03_18

## Slide 10
EA (Actual Exposure)
G.13.1.1
DAPIMB (Daily Average Imbalance Settlement Price)
G.14.2.1
NDAPIMB (# Daily Average Imbalance Settlement Prices)
G.14.2.2
UMPIMB (mean Daily Average Imbalance Settlement Prices)
G.14.2.3
SDPIMB (stdev Daily Average Imbalance Settlement Prices)
G.14.2.4
PCA (Credit Assessment Price)
G.14.2.5
CCAP (Combined Credit Assessment Price)
G.14.2.6
EUPES (Exposure for Trading, Supplier Units)
G.14.3.2
VCAS (Credit Assessment Volume for Supplier Units)
G.14.3.1
EUPECC (Exposure for Capacity Charges)
G.14.3.3 (NorA)
VCAG (Credit Assessment Volume for Generator Units)
G.14.4.1
EUPEG (Exposure for Trading, Generator Units)
G.14.4.2
BPHAP (# Sample Undefined Exposure Periods in HAP)
G.14.7.2
QMB (Billing Period Metered Demand, Supplier Units)
G.14.7.3
QMBM (mean Billing Period Metered Demand, Supplier Units)
G.14.7.4
QMBSD (stdev Billing Period Metered Demand, Supplier Units)
G.14.7.5
QUPEB (Billing Period Undefined Potential Exposure, Supplier Units)
G.14.7.6
EUPES (Exposure for Trading, Supplier Units)
G.14.7.7 (Std)
EUPECC (Exposure for Capacity Charges)
G.14.8.1 (Std)
CUB (Billing Period Cashflow, Generator Units)
G.14.10.1 (Std)
CUBM (mean Billing Period Cashflow, Generator Units)
G.14.10.2 (Std)
CUBSD (stdev Billing Period Cashflow, Generator Units)
G.14.10.3 (Std)
EUPEG (Exposure for Trading, Generator Units)
G.14.10.4 (Std)
CUB (Billing Period Cashflow, Assetless Units)
G.14.12.1 (Std)
CUBM (mean Billing Period Cashflow, Assetless Units)
G.14.12.2 (Std)
CUBSD (stdev Billing Period Cashflow, Assetless Units)
G.14.12.3 (Std)
EUPEG (Exposure for Trading, Assetless Units)
G.14.12.4 (Std)
ETND (Traded Not Delivered Exposure)
G.14.13.1
EUPECP (Undefined Exposure for Capacity Payments
G.14.14.1 (All)
FAVRA (Forecast for SRAs)
G.14.15.2 (All)
EC_BILIMB (Energy Credit for Secondary PT)
G.14.15.4 (All)
CC_BILCAP (Capacity Credit for Secondary PT)
G.14.15.5 (All)
EC_UNBIMB (Risk Period Energy Credit for Secondary PT)
G.14.15.6 (All)
CC_UNBCAP (Risk Period Energy Credit for Secondary PT)
G.14.15.7 (All)
FAVRA (Forecast for SRAs, Secondary PT)
G.14.15.8 (All)
FASRAS (Forecast for SRAs, Secondary PT)
G.14.15.9 (All)
FASRAP (Forecast for SRAs, Principal PT)
G.14.15.10 (All)
SRAs
Required Credit Cover Determinants
Required Credit Cover
RCC (Required Credit Cover)
G.15.1.1
Credit Assessment Prices and Volumes
Undefined Exposure for Supplier Units
(Standard PT)
Undefined Exposure for Generator Units
(Standard PT)
Undefined Exposure for Assetless Units
(Standard PT)
FCR (Fixed Credit Requirement)
G.10.1.1 (All)
Undefined Exposure for Supplier Units
(New/Adjusted PT)
Undefined Exposure for Generator Units
(New/Adjusted PT)
Non-Participant-Specific values
Participant-Specific values
Summary of TSC Credit Cover Provisions

## Slide 11
EA (Actual Exposure)
G.13.1.1
DAPIMB (Daily Average Imbalance Settlement Price)
G.14.2.1
NDAPIMB (# Daily Average Imbalance Settlement Prices)
G.14.2.2
UMPIMB (mean Daily Average Imbalance Settlement Prices)
G.14.2.3
SDPIMB (stdev Daily Average Imbalance Settlement Prices)
G.14.2.4
PCA (Credit Assessment Price)
G.14.2.5
CCAP (Combined Credit Assessment Price)
G.14.2.6
EUPES (Exposure for Trading, Supplier Units)
G.14.3.2
VCAS (Credit Assessment Volume for Supplier Units)
G.14.3.1
EUPECC (Exposure for Capacity Charges)
G.14.3.3 (NorA)
VCAG (Credit Assessment Volume for Generator Units)
G.14.4.1
EUPEG (Exposure for Trading, Generator Units)
G.14.4.2
BPHAP (# Sample Undefined Exposure Periods in HAP)
G.14.7.2
QMB (Billing Period Metered Demand, Supplier Units)
G.14.7.3
QMBM (mean Billing Period Metered Demand, Supplier Units)
G.14.7.4
QMBSD (stdev Billing Period Metered Demand, Supplier Units)
G.14.7.5
QUPEB (Billing Period Undefined Potential Exposure, Supplier Units)
G.14.7.6
EUPES (Exposure for Trading, Supplier Units)
G.14.7.7 (Std)
EUPECC (Exposure for Capacity Charges)
G.14.8.1 (Std)
CUB (Billing Period Cashflow, Generator Units)
G.14.10.1 (Std)
CUBM (mean Billing Period Cashflow, Generator Units)
G.14.10.2 (Std)
CUBSD (stdev Billing Period Cashflow, Generator Units)
G.14.10.3 (Std)
EUPEG (Exposure for Trading, Generator Units)
G.14.10.4 (Std)
CUB (Billing Period Cashflow, Assetless Units)
G.14.12.1 (Std)
CUBM (mean Billing Period Cashflow, Assetless Units)
G.14.12.2 (Std)
CUBSD (stdev Billing Period Cashflow, Assetless Units)
G.14.12.3 (Std)
EUPEG (Exposure for Trading, Assetless Units)
G.14.12.4 (Std)
ETND (Traded Not Delivered Exposure)
G.14.13.1
EUPECP (Undefined Exposure for Capacity Payments
G.14.14.1 (All)
FAVRA (Forecast for SRAs)
G.14.15.2 (All)
EC_BILIMB (Energy Credit for Secondary PT)
G.14.15.4 (All)
CC_BILCAP (Capacity Credit for Secondary PT)
G.14.15.5 (All)
EC_UNBIMB (Risk Period Energy Credit for Secondary PT)
G.14.15.6 (All)
CC_UNBCAP (Risk Period Energy Credit for Secondary PT)
G.14.15.7 (All)
FAVRA (Forecast for SRAs, Secondary PT)
G.14.15.8 (All)
FASRAS (Forecast for SRAs, Secondary PT)
G.14.15.9 (All)
FASRAP (Forecast for SRAs, Principal PT)
G.14.15.10 (All)
SRAs
Required Credit Cover Determinants
Required Credit Cover
RCC (Required Credit Cover)
G.15.1.1
Credit Assessment Prices and Volumes
Undefined Exposure for Supplier Units
(Standard PT)
Undefined Exposure for Generator Units
(Standard PT)
Undefined Exposure for Assetless Units
(Standard PT)
FCR (Fixed Credit Requirement)
G.10.1.1 (All)
Undefined Exposure for Supplier Units
(New/Adjusted PT)
Undefined Exposure for Generator Units
(New/Adjusted PT)
Non-Participant-Specific values
Participant-Specific values
Summary of TSC Credit Cover Provisions
System calculation change
Description change only

## Slide 12: End

## Slide 13: Autoproducers Credit Calculation AUGHINISH Alumina Ltd
Jan 2018

## Slide 14: Aughinish historic delivery Freq Distribution over 10 years
Delivery at 110MW
Or
Delivery at 35MW
Consumption <10MW
2nd Tuesday in May
99.6% availability in 2017

## Slide 15: Autoproducer Problem Structure in the I-SEM TSC Part B
Party PY_000024 Aughinish Alumina ltd
Participant
PT_400024
TS_400031 (Trading Site Account)
SK3 GU_400120
PPTG
SK4 GU_400121
PPTG
TSSU SU_400030
TU_400001 Trading Unit
Netting Generator Unit Removed
-115MW
Q imb
+80MW
+80MW
-45MW

## Slide 16: Autoproducer Problem Physical units
SK3
80MW
SK4 80MW
In-house
45MW
Station gate Delivery 115MW and
QExAnte = 115MW
SK3
80MW
SK4 80MW
In-house
45MW
QM NGU TSSU - 45MW
QM SK4 80MW
QM SK3 80MW
Balancing Market Units
TU
Virtual
QM TU =0 MW but QExAnte = 115MW
Notes: This is what we do
This is what an Autoproducer is intended to represent in the TSC Part A, B & C

## Slide 17: Autoproducer Problem Physical units
Balancing Market Units
115MW Autoproducer
Qimb = +160MW and -160MW
115MW Generator
Qimb = +0MW
Notes: This is what we do
This is what an Autoproducer is intended to represent in the TSC Part A, B & C

## Slide 18: Implication Autoproducer Excess Collateral (100% balance responsible)
€800,000

## Slide 19: The I-SEM Solution
New section G.14.17.1
To calculate the Billing Period Cashflow for an Autoproducer as follows
New section G.14.17.4
can be positive or negative
If CUBMpg => 0 then:
If CUBMpg < 0 then:
For all Units
GU Cashflow
CMU Cashflow
SU Cashflow
Registered to an Autoproducer Site
In
Settlement Day, d
For all
d in Sample Undefined Exposure Period, ω

## Slide 20: Justification
Changes only affect Trading Site with a contiguous Autoproducer
Provides for equal treatment for all participants
Over collateralisation (by one participant)
Bar DAM trading
  Spill into BM
  Counter intuitive trading
  Reduce liquidity in DAM
Would jeopardies the 700 jobs on site in West Limerick.
  The alternative price of steam would be uncompetitive in a global alumina market.
Increased carbon emissions
Discourages further investment in High Efficiency CHP

## Slide 21: Conclusion
This is a correction of the code it aligns credit Calc with settlement of an Autoproducer
Autoproducers ExAnte trades (Trading Unit) are matched from their physical units. Qimb = +160MW and -160MW
Any participant should only be exposed to their imbalance position
Must be implemented for go-live